## Slide 1: PAX DETECTOR
THERMAL SIMULATION

## Slide 2: PAX DETECTOR FEM* ASSEMBLY LAYOUT
HEAT FLUX
COOLING PLATE
ELECTRONIC SUPPORT
COOLING TUBE
TARGET CELL
SILICON DETECTOR
VACUUM CHAMBER
SILICON SUPPORT
* FEM = Finite Element Modeler

## Slide 3
PARTS MATERIALS | 
PART | MATERIAL
SILICON DETECTOR | SILICON
TARGET CELL | ALUMINUM
SILICON SUPPORT | ALUMINUM
ELECTRONIC SUPPORT | ALUMINUM
VACUUM CHAMBER | STAINLESS STEEL
MATERIAL PROPERTIES |  |  |  | 
MATERIAL | DENSITY (Kg/m^3) | THERMAL CONDUCTIVITY (W/mK) | EMISSIVITY (*) | SPECIFIC HEAT (J/KgK)
ALUMINUM | 2700 | 237 | 0.09 | 900
STAINLESS STEEL | 7960 | 16,3 | 0,16 | 502
SILICON | 2340 | 115 | 0,9 | 703
MATERIALS
(*)
From the Engineering Toolbox (www.engineeringtoolbox.com)

## Slide 4
THE ANALISYS
THE FOLLOWING ANALISYS HAVE BEEN PERFORMED :
RADIATION ANALISYS
SIMULATION EVALUATING THE AMOUNT OF HEAT LOAD COMING FROM RADIATION
TEMPERATURE ANALISYS
SIMULATION EVALUATING THE DETECTOR’S TEMPERATURE DISTRIBUTION COMING FROM ELECTRONIC POWER AND RADIATION

## Slide 5
RADIATION ANALISYS
SILICON SUPPORT SET AT CONSTANT TEMPERATURE
ELCTRONIC POWER SWITCHED OFF
VACUUM CHAMBER SET AT CONSTANT TEMPERATURE
CONSTANT TEMPERATURE
VACUUM CHAMBER
SILICON SUPPORT

## Slide 6
FEM RADIATION ANALYSIS BCs |  |  |  |  |  | 
 | SILICON DETECTOR | SILICON SUPPORT | COOLING TUBE | TARGET CELL | ELECTRONIC & SUPPORT | VACUUM CHAMBER
RADIATIVE THERMAL COUPLINGS | TO ALL PARTS | TO ALL PARTS |  | TO ALL PARTS |  | TO ALL PARTS
CONDUCTIVE THERMAL COUPLINGS | TO SILICON SUPPORT |  |  |  |  | 
CONSTANT TEMPERATURES (C°) |  | -20 |  |  |  | 20 ; 40 ; 60
HEAT LOAD (W) |  |  |  |  | SWITCHED OFF | 
RADIATION ANALYSIS BOUNDARY CONDITIONS
ADDITIONAL INFORMATIONS
§ - SHADOWING CHECKS BETWEEN PARTS PERMORMED

## Slide 7
BOUNDARY CONDITIONS |  | 
 | SILICON SUPPORT SURFACES CONSTANT TEMP (C°) | VACUUM CHAMBER WALLS CONSTANT TEMP (C°)
1° Analysis | -20 | 20
2° Analysis | -20 | 40
3° Analysis | -20 | 60
RADIATION ANALYSIS RESULTS |  |  |  |  |  | 
PART | 1° ANALYSIS |  | 2° ANALYSIS |  | 3° ANALYSIS | 
 | AVERAGE TEMP (C°) | POWER (W) | AVERAGE TEMP (C°) | POWER (W) | AVERAGE TEMP (C°) | POWER (W)
SILICON DETECTOR | -18,3 | -22,47 | -17,6 | -21,81 | -16,7 | -21,00
SILICON SUPPORT |  | 63,68 |  | 91,27 |  | 124,7
TARGET CELL | -17 | -0,104 | -15,5 | -0.096 | -13,5 | -0.085
VACUUM CHAMBER |  | -41,10 |  | -69,37 |  | -103,6
RADIATION ANALYSIS RESULTS
Chart: 2° ANALISYS - SHARED POWER %
| 2
VACUUM CHAMBER | 76.0053
SILICON DETECTOR | 23.8961
TARGET CELL | 0.10518

## Slide 8
TEMPERATURE ANALISYS
COOLING TUBE WALL SET AT CONSTANT TEMPERATURE
ELCTRONIC POWER SWITCHED ON
COOLING TUBE
ELECTRONIC POWER

## Slide 9
FEM TEMPERATURE ANALYSIS BCs |  |  |  |  |  | 
 | SILICON DETECTOR | SILICON SUPPORT | COOLING TUBE | TARGET CELL | ELECTRONIC & SUPPORT | VACUUM CHAMBER
RADIATIVE THERMAL COUPLINGS | TO ALL PARTS | TO ALL PARTS |  | TO ALL PARTS | VACUUM CHAMBER & SILICON SUPPORT | TO ALL PARTS
CONDUCTIVE THERMAL COUPLINGS | TO SILICON SUPPORT |  | TO SILICON SUPPORT |  |  | 
CONSTANT TEMPERATURES (C°) |  |  | -20 |  |  | 
HEAT LOAD (W) |  |  |  |  | 85 | 
TEMPERATURE ANALYSIS BOUNDARY CONDITIONS
ADDITIONAL INFORMATIONS
§ - SHADOWING CHECKS BETWEEN PARTS PERMORMED
§ - ENVIRONMENT TEMPERATURE = 25 C°

## Slide 10
BOUNDARY CONDITIONS | 
ENVIRONMENT TEMPERATURE = 25 C° | 
COOLING TUBE WALL TEMP (C°) | ELECTRONIC HEAT LOAD (W)
-20 | 85
ANALYSIS RESULTS |  |  | 
PART | TEMPERATURE (C°) |  | POWER (W)
 | Tmin | Tmax | 
SILICON DETECTOR | -19,5 | -12,8 | -32,4
SILICON SUPPORT | -20 | -16,6 | -4
TARGET CELL | -11,9 | -11,7 | -1,5
COOLING TUBE WALL | -20 | -20 | 117,2
ELECTRONIC |  |  | -85,00
VACUUM CHAMBER | 28 | 31 | 5,7
TEMPERATURE ANALYSIS RESULTS
Chart: SHARED POWER %
| 2
ELECTRONIC | 69.2
SILICON DETECTOR | 26.4
SILICON SUPPORT | 3.3
TARGET CELL | 1.2

## Slide 11: SILICON SUPPORT – TEMPERATURE DISTRIBUTION Tmin = -20 C° ; Tmax = -16,6 C°

## Slide 12: SILICON DETECTOR – TEMPERATURE DISTRIBUTION Tmin = -19,5 C° ; Tmax = -12,8 C°

## Slide 13: TARGET CELL – TEMPERATURE DISTRIBUTION Tmin = -11,9 C° ; Tmax = -11,7 C°

## Slide 14: DETECTOR ASSEMBLY – TEMPERATURE DISTRIBUTION

## Slide 15: COOLING DESIGN
TOTAL COOLING POWER (4/4)

## Slide 16: COOLING DESIGN
COOLING FLUID : ETHANOL ALCOHOOL |  | °C | W/m^2C°
Boiling point |  | 78,5 | 
Freezing point |  | -114 | 
Convection coefficient | α |  | 170
Delivery temperature | Td | -41 | 
Wall temperature | Tw | -20 | 
Fluid temperature | Tf = (Td + Tw)/2 | -30,5 | 
ETHANOL PROPERTIES @ Tf and atmospheric pressure |  | 
Density (Kg/m^3) | ρ | 832
Specific heat (J/KgK) | Cp | 2215
Thermal conductivity (W/mK) | λ | 0,13
Kinematic viscosity (m^2/s) | ν | 3,23E-06
Kinematic viscosity @ Tw (m^2/s) | νw | 2,88E-06
Chart: fuid temperature @ Twall = -20 C° & Dtube = 8 mm
| 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 300
Tfluid | -76.8699 | -48.4349 | -38.9566 | -34.2175 | -31.374 | -29.4783 | -28.1243 | -27.1087 | -26.3189 | -25.687 | -25.17 | -24.7392
Tdelivery | -133.7398 | -76.8699 | -57.9133 | -48.4349 | -42.748 | -38.9566 | -36.2485 | -34.2175 | -32.6378 | -31.374 | -30.34 | -29.4783
COOLING FLUID TEMPERATURE VS CONVECTION COEFFICIENT
COOLING FLUID & CONVECTION COEFFICIENT SELECTION

## Slide 17: COOLING DESIGN
FLOW SPEED, FLOW RATE AND PRESSURE LOSS
Chart: α (W/m^2C°)
| 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 300
flow rate (Kg/h) | 0.1 | 0.34 | 0.83 | 1.64 | 2.87 | 4.6 | 6.9 | 9.9 | 13.6 | 18.2 | 23.7 | 30.2
flow speed (m/min) | 0.04 | 0.132 | 0.3264 | 0.648 | 1.14 | 1.8 | 2.76 | 3.96 | 5.4 | 7.2 | 9.6 | 12
Tfluid (C°) d=8 | -76.8699 | -48.4349 | -38.9566 | -34.2175 | -31.374 | -29.4783 | -28.1243 | -27.1087 | -26.3189 | -25.687 | -25.17 | -24.7392
Tdelivery (C°) d=8 | -133.7398 | -76.8699 | -57.9133 | -48.4349 | -42.748 | -38.9566 | -36.2485 | -34.2175 | -32.6378 | -31.374 | -30.34 | -29.4783

## Slide 18
CONCLUSIONS
A THERMAL ANALISYS INVESTIGATING THE RADIATION EFFECTS ON THE SILICON DETECTOR HAS BEEN DONE.
A SUPPLEMENTARY ANALISYS CONSIDERING BOTH THE ELECTRONIC POWER AND THE RADIATION HAS BEEN ALSO SIMULATED.
AN IMPROVEMENT OF THE ANALISYS RESULTS CAN BE ACHIEVED , GIVEN THE FOLLOWING INFORMATIONS :
AVERAGE WORKING TEMPERATURE OF THE SILICON DETECTOR
VALUE OF THE ELECTRONIC POWER