## Slide 1: Pipelined protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 2: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may deceive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 3: GBN: sender extended FSM

## Slide 4: GBN: receiver extended FSM
receiver simple:
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  ACK pkt with highest in-order seq #

## Slide 5: GBN in action

## Slide 6: Selective Repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  again limits seq #s of sent, unACKed pkts

## Slide 7: Selective repeat: sender, receiver windows

## Slide 8: Selective repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 9: Selective repeat in action

## Slide 10: Selective repeat: dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)
Q: what relationship between seq # size and window size?

## Slide 11: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 12: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 13: TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 14: TCP: reliable data transfer
simplified sender, assuming
wait
for
event
wait
for
event
event: data received
from application above
event: timer timeout for
segment with seq # y
event: ACK received,
with ACK # y
create, send segment
retransmit segment
ACK processing
one way data transfer
no flow, congestion control

## Slide 15: TCP ACK generation [RFC 1122, RFC 2581]
Event
in-order segment arrival,
no gaps,
everything else already ACKed
in-order segment arrival,
no gaps,
one delayed ACK pending
out-of-order segment arrival
higher-than-expect seq. #
gap detected
arrival of segment that
partially or completely fills gap
TCP Receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single
cumulative ACK
send duplicate ACK, indicating seq. #
of next expected byte
immediate ACK if segment starts
at lower end of gap

## Slide 16: TCP: retransmission scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
time
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
Host A
Seq=100, 20 bytes data
ACK=100
Seq=92 timeout
time
premature timeout,
cumulative ACKs
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=100 timeout
ACK=120

## Slide 17: TCP Flow Control
receiver: explicitly informs sender of (dynamically changing) amount of free buffer space
  RcvWindow field in TCP segment
sender: keeps the amount of transmitted, unACKed data less than most recently received RcvWindow
sender won’t overrun
receiver’s buffers by
transmitting too much,
too fast
flow control
receiver buffering
RcvBuffer = size of TCP Receive Buffer
RcvWindow = amount of spare room in Buffer