## Slide 1: Application use case : Secure e-mail
generates random symmetric private key, KS.
encrypts message with KS
also encrypts KS with Bob’s public key.
sends both KS(m) and eB(KS) to Bob.
Alice wants to send secret e-mail message, m, to Bob.

## Slide 2: Secure e-mail (continued)
Alice wants to provide sender authentication and message integrity.
Alice digitally signs message.
sends both message (in the clear) and digital signature.

## Slide 3: Secure e-mail (continued)
Alice wants to provide secrecy, sender authentication, message integrity.
Note: Alice uses both her private key, Bob’s public key.

## Slide 4: Pretty good privacy (PGP)
Internet e-mail encryption scheme, a de-facto standard.
Uses symmetric key cryptography, public key cryptography, hash function, and digital signature as described.
Provides secrecy, sender authentication, integrity.
---BEGIN PGP SIGNED MESSAGE---
Hash: SHA1
Bob:My husband is out of town tonight.Passionately yours, Alice
---BEGIN PGP SIGNATURE---
Version: PGP 5.0
Charset: noconv
yhHJRHhGJGhgg/12EpJ+lo8gE4vB3mqJhFEvZP9t6n7G6m5Gw2
---END PGP SIGNATURE---
A PGP signed message:

## Slide 5: Secure sockets layer (SSL)
PGP provides security for a specific network app.
SSL works at transport layer. Provides security to any TCP-based app using SSL services.
SSL: used between WWW browsers, servers for E-commerce (https).
SSL security services:
  server authentication
  data encryption
  client authentication (optional)
Server authentication:
  SSL-enabled browser includes public keys for trusted CAs.
  Browser requests server certificate, issued by trusted CA.
  Browser uses CA’s public key to extract server’s public key from certificate.
Visit your browser’s security menu to see its trusted CAs.

## Slide 6: SSL (continued)
Encrypted SSL session:
Browser generates symmetric session key, encrypts it with server’s public key, sends encrypted key to server.
Using its private key, server decrypts session key.
Browser, server agree that future msgs will be encrypted.
All data sent into TCP socket (by client or server) encrypted with session key.
SSL: basis of IETF Transport Layer Security (TLS).
SSL can be used for non-Web applications, e.g., IMAP.
Client authentication can be done with client certificates.

## Slide 7: Secure electronic transactions (SET)
designed for payment-card transactions over Internet.
provides security services among 3 players:
  customer
  merchant
  merchant’s bank
  All must have certificates.
SET specifies legal meanings of certificates.
  apportionment of liabilities for transactions
Customer’s card number passed to merchant’s bank without merchant ever seeing number in plain text.
  Prevents merchants from stealing, leaking payment card numbers.
Three software components:
  Browser wallet
  Merchant server
  Acquirer gateway
See documentation for description of SET transaction.

## Slide 8: IPsec: Network Layer Security
Network-layer secrecy:
  sending host encrypts the data in IP datagram
  TCP and UDP segments; ICMP and SNMP messages.
Network-layer authentication
  destination host can authenticate source IP address
Two principle protocols:
  authentication header (AH) protocol
  encapsulation security payload (ESP) protocol
For both AH and ESP, source, destination handshake:
  create network-layer logical channel called a service agreement (SA)
Each SA unidirectional.
Uniquely determined by:
  security protocol (AH or ESP)
  source IP address
  32-bit connection ID

## Slide 9: Authentication Header (AH) Protocol
Provides source host authentication, data integrity, but not secrecy.
AH header inserted between IP header and IP data field.
Protocol field = 51.
Intermediate routers process datagrams as usual.
AH header includes:
connection identifier
authentication data: signed message digest, calculated over original IP datagram, providing source authentication, data integrity.
Next header field: specifies type of data (TCP, UDP, ICMP, etc.)

## Slide 10: ESP Protocol
Provides secrecy, host authentication, data integrity.
Data, ESP trailer encrypted.
Next header field is in ESP trailer.
ESP authentication field is similar to AH authentication field.
Protocol = 50.

## Slide 11: Network Security (summary)
Basic techniques…...
cryptography (symmetric and public)
authentication
message integrity
…. used in many different security scenarios
secure email
secure transport (SSL)
IP sec