## Slide 1: IEEE 802.11 Wireless LAN
wireless LANs: untethered (often mobile) networking
IEEE 802.11 standard:
  MAC protocol
  unlicensed frequency spectrum: 900Mhz, 2.4Ghz
BSS’s combined to form distribution system (DS)
Basic Service Set (BSS) (a.k.a. “cell”) contains:
  wireless hosts
  access point (AP): base station

## Slide 2: Ad Hoc Networks
Ad hoc network: IEEE 802.11 stations can dynamically form network without AP
Applications:
  “laptop” meeting in conference room, car
  interconnection of “personal” devices
IETF MANET (Mobile Ad hoc Networks) working group

## Slide 3: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 CSMA: sender
- if sense channel idle for DIFS (Distr. Inter Frame Space) sec.
then transmit entire frame (no collision detection)
-if sense channel busy then binary backoff
802.11 CSMA receiver:
if received OK
return ACK after SIFS (Short Inter Frame Spacing)

## Slide 4: IEEE 802.11 MAC Protocol
802.11 CSMA Protocol: others
NAV: Network Allocation Vector
802.11 frame has transmission time field
others (hearing data) defer access for NAV time units

## Slide 5: Hidden Terminal effect
hidden terminals: A, C cannot hear each other
  obstacles, signal attenuation
  collisions at B
goal: avoid collisions at B
CSMA/CA: CSMA with Collision Avoidance
Threshold

## Slide 6: Collision Avoidance: RTS-CTS exchange
CSMA/CA: explicit channel reservation
  sender: send short RTS: request to send
  receiver: reply with short CTS: clear to send
CTS reserves channel for sender, notifying (possibly hidden) stations
avoid hidden station collisions

## Slide 7: Collision Avoidance: RTS-CTS exchange
RTS and CTS short:
  collisions less likely, of shorter duration
  end result similar to collision detection
IEEE 802.11 allows:
  CSMA
  CSMA/CA: reservations
  polling from AP

## Slide 8: Point to Point Data Link Control
one sender, one receiver, one link: easier than broadcast link:
  no Media Access Control
  no need for explicit MAC addressing
  e.g., dialup link, ISDN line
popular point-to-point DLC protocols:
  PPP (point-to-point protocol)
  HDLC: High level Data Link Control (Data link used to be considered “high layer” in protocol stack!)

## Slide 9: PPP Design Requirements [RFC 1557]
packet framing: encapsulation of network-layer datagram in data link frame
  carry network layer data of any network layer protocol (not just IP) at same time
  ability to demultiplex upwards
bit transparency: must carry any bit pattern in the data field
error detection (no correction)
connection state: detect, signal link failure to network layer
network layer address negotiation: endpoint can learn/configure each other’s network address

## Slide 10: PPP non-requirements
no error correction/recovery
no flow control
out of order delivery OK
no need to support multipoint links (e.g., polling)
Error recovery, flow control, data re-ordering
all relegated to higher layers!|

## Slide 11: PPP Data Frame
Flag: delimiter (framing)
Address: does nothing (only one option)
Control: does nothing; in the future possible multiple control fields
Protocol: upper layer protocol to which frame delivered (eg, PPP-LCP, IP, IPCP, etc)

## Slide 12: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 13: Asynchronous Transfer Mode: ATM
1980s/1990’s standard for high-speed (155Mbps to 622 Mbps and higher) Broadband Integrated Service Digital Network architecture
Goal: integrated, end-end transport of carry voice, video, data
  meeting timing/QoS requirements of voice, video (versus Internet best-effort model)
  “next generation” telephony: technical roots in telephone world
  packet-switching (fixed length packets, called “cells”) using virtual circuits

## Slide 14: ATM architecture
adaptation layer: only at edge of ATM network
  data segmentation/reassembly
  roughly analagous to Internet transport layer
ATM layer: “network” layer
  cell switching, routing
physical layer

## Slide 15: ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  ATM is a network technology
Reality: used to connect IP backbone routers
  “IP over ATM”
  ATM as switched link layer, connecting IP routers

## Slide 16: ATM Adaptation Layer (AAL)
ATM Adaptation Layer (AAL): “adapts” upper layers (IP or native ATM applications) to ATM layer below
AAL present only in end systems, not in switches
AAL layer segment (header/trailer fields, data) fragmented across multiple ATM cells
  analogy: TCP segment in many IP packets

## Slide 17: ATM Adaption Layer (AAL) [more]
Different versions of AAL layers, depending on ATM service class:
AAL1: for CBR (Constant Bit Rate) services, e.g. circuit emulation
AAL2: for VBR (Variable Bit Rate) services, e.g., MPEG video
AAL5: for data (eg, IP datagrams)
AAL PDU
ATM cell
User data

## Slide 18: ATM Layer
Service: transport cells across ATM network
analagous to IP network layer
very different services than IP network layer
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 19: ATM Layer: Virtual Circuits
VC transport: cells carried on VC from source to dest
  call setup, teardown for each call before data can flow
  each packet carries VC identifier (not destination ID)
  every switch on source-dest path maintain “state” for each passing connection
  link,switch resources (bandwidth, buffers) may be allocated to VC: to get circuit-like perf.
Permanent VCs (PVCs)
  long lasting connections
  typically: “permanent” route between IP routers
Switched VCs (SVC):
  dynamically set up on per-call basis

## Slide 20: ATM VCs
Advantages of ATM VC approach:
  QoS performance guarantee for connection mapped to VC (bandwidth, delay, delay jitter)
Drawbacks of ATM VC approach:
  Inefficient support of datagram traffic
  one PVC between each source/dest pair, does not scale (N*2 connections needed)
  SVC introduces call setup latency, processing overhead for short lived connections

## Slide 21: ATM Layer: ATM cell
5-byte ATM cell header
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
Cell header
Cell format

## Slide 22: ATM cell header
VCI: virtual channel ID
PT: Payload type (e.g. RM cell versus data cell)
CLP: Cell Loss Priority bit
  CLP = 1 implies low priority cell, can be discarded if congestion
HEC: Header Error Checksum
  cyclic redundancy check

## Slide 23: ATM Physical Layer (more)
Two pieces (sublayers) of physical layer:
Transmission Convergence Sublayer (TCS): adapts ATM layer above to PMD sublayer below
Physical Medium Dependent: depends on physical medium being used
TCS Functions:
  Header checksum generation: 8 bits CRC
  Cell delineation
  With “unstructured” PMD sublayer, transmission of idle cells when no data cells to send

## Slide 24: ATM Physical Layer
Physical Medium Dependent (PMD) sublayer
SONET/SDH: transmission frame structure (like a container carrying bits);
  bit synchronization;
  bandwidth partitions (TDM);
  several speeds: OC1 = 51.84 Mbps; OC3 = 155.52 Mbps; OC12 = 622.08 Mbps
TI/T3: transmission frame structure (old telephone hierarchy): 1.5 Mbps/ 45 Mbps
unstructured: just cells (busy/idle)

## Slide 25: IP-Over-ATM
Classic IP only
3 “networks” (e.g., LAN segments)
MAC (802.3) and IP addresses
IP over ATM
replace “network” (e.g., LAN segment) with ATM network
ATM addresses, IP addresses
ATM
network
Ethernet
LANs
Ethernet
LANs

## Slide 26: IP-Over-ATM
Issues:
IP datagrams into ATM AAL5 PDUs
from IP addresses to ATM addresses
  just like IP addresses to 802.3 MAC addresses!
ATM
network
Ethernet
LANs

## Slide 27: Datagram Journey in IP-over-ATM Network
at Source Host:
  IP layer finds mapping between IP, ATM dest address (using ARP)
  passes datagram to AAL5
  AAL5 encapsulates data, segments to cells, passes to ATM layer
ATM network: moves cell along VC to destination
at Destination Host:
  AAL5 reassembles cells into original datagram
  if CRC OK, datgram is passed to IP

## Slide 28: ARP in ATM Nets
ATM network needs destination ATM address
  just like Ethernet needs destination Ethernet address
IP/ATM address translation done by ATM ARP (Address Resolution Protocol)
  ARP server in ATM network performs broadcast of ATM ARP translation request to all connected ATM devices
  hosts can register their ATM addresses with server to avoid lookup

## Slide 29: X.25 and Frame Relay
Like ATM:
wide area network technologies
virtual circuit oriented
origins in telephony world
can be used to carry IP datagrams
  can thus be viewed as Link Layers by IP protocol

## Slide 30: X.25
X.25 builds VC between source and destination for each user connection
Per-hop control along path
  error control (with retransmissions) on each hop
    variant of the HDLC protocol
  per-hop flow control using credits
    congestion arising at intermediate node propagates to previous node on path
    back to source via back pressure

## Slide 31: IP versus X.25
X.25: reliable in-sequence end-end delivery from end-to-end
  “intelligence in the network”
IP: unreliable, out-of-sequence end-end delivery
  “intelligence in the endpoints”
gigabit routers: limited processing possible
2000: IP wins

## Slide 32: Frame Relay
Designed in late ‘80s, widely deployed in the ‘90s
Frame relay service:
  no error control
  end-to-end congestion control

## Slide 33: Frame Relay (more)
Designed to interconnect corporate customer LANs
  typically permanent VC’s: “pipe” carrying aggregate traffic between two routers
  switched VC’s: as in ATM
corporate customer leases FR service from public Frame Relay network (eg, Telecom,Sprint, ATT)

## Slide 34: Frame Relay -VC Rate Control
Committed Information Rate (CIR)
  defined, “guaranteed” for each VC
  negotiated at VC set up time
  customer pays based on CIR
DE bit: Discard Eligibility bit
  Edge FR switch measures traffic rate for each VC; marks DE bit
  DE = 0: high priority, rate compliant frame; deliver at “all costs”
  DE = 1: low priority, eligible for discard when congestion

## Slide 35: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing, ARP
various link layer technologies
  Ethernet
  hubs, bridges, switches
  IEEE 802.11 LANs
  PPP
  ATM
  X.25, Frame Relay
journey down the protocol stack now OVER!