## Slide 1: Network Layer
Chapter goals:
understand principles behind network layer services:
  routing (path selection)
  dealing with scale
  how a router works
  advanced topics: IPv6, multicast
instantiation and implementation in the Internet
Overview:
network layer services
routing principle: path selection
hierarchical routing
IP
Internet routing protocols reliable transfer
  intra-domain
  inter-domain
what’s inside a router?
IPv6
multicast routing

## Slide 2: Network layer functions
transport packet from sending to receiving hosts
network layer protocols in every host, router
three important functions:
path determination: route taken by packets from source to dest. Routing algorithms
switching: move packets from router’s input to appropriate router output
call setup: some network architectures require router call setup along path before data flows
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 3: Network service model
Q: What service model for “channel” transporting packets from sender to receiver?
guaranteed bandwidth?
preservation of inter-packet timing (no jitter)?
loss-free delivery?
in-order delivery?
congestion feedback to sender?
?
?
?
virtual circuit
or
datagram?
The most important
abstraction provided
by network layer:
service abstraction

## Slide 4: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host ID)
every router on source-dest path s maintain “state” for each passing connection
  transport-layer connection only involved two end systems
link, router resources (bandwidth, buffers) may be allocated to VC
  to get circuit-like perf.
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 5: Virtual circuits: signaling protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 6: Datagram networks: the Internet model
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets typically routed using destination host ID
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 7: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 8: Datagram or VC network: why?
Internet
data exchange among computers
  “elastic” service, no strict timing req.
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
many link types
  different characteristics
  uniform service difficult
ATM
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 9: Routing
Graph abstraction for routing algorithms:
graph nodes are routers
graph edges are physical links
  link cost: delay, $ cost, or congestion level
Goal: determine “good” path
(sequence of routers) thru
network from source to dest.
Routing protocol
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
“good” path:
  typically means minimum cost path
  other def’s possible

## Slide 10: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 11: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives routing table for that node
iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(i,j): link cost from node i to j. cost infinite if not direct neighbors
D(v): current value of cost of path from source to dest. V
p(v): predecessor node along path from source to v, that is next v
N: set of nodes whose least cost path definitively known

## Slide 12: Dijsktra’s Algorithm
1 Initialization:
2 N = {A}
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v)
6 else D(v) = infty
7
8 Loop
9 find w not in N such that D(w) is a minimum
10 add w to N
11 update D(v) for all v adjacent to w and not in N:
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N

## Slide 13: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
start N
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
2,A
2,A
D(C),p(C)
5,A
4,D
3,E
3,E
D(D),p(D)
1,A
D(E),p(E)
infinity
2,D
D(F),p(F)
infinity
infinity
4,E
4,E
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 14: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n*(n+1)/2 comparisons: O(n**2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
A
D
C
B
2+e
0
0
0
1+e
1
A
D
C
B
0
2+e
1+e
1
0
0
A
D
C
B
2+e
0
e
0
1+e
1
initially
… recompute
routing
… recompute
… recompute

## Slide 15: Distance Vector Routing Algorithm
iterative:
continues until no nodes exchange info.
self-terminating: no “signal” to stop
asynchronous:
nodes need not exchange info/iterate in lock step!
distributed:
each node communicates only with directly-attached neighbors
Distance Table data structure
each node has its own
row for each possible destination
column for each directly-attached neighbor to node
example: in node X, for dest. Y via neighbor Z:
D (Y,Z)
X
distance from X to
Y, via Z as next hop
c(X,Z) + min {D (Y,w)}
Z
w
=
=

## Slide 16: Distance Table: example
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
D (C,D)
E
c(E,D) + min {D (C,w)}
D
w
=
=
2+2 = 4
D (A,D)
E
c(E,D) + min {D (A,w)}
D
w
=
=
2+3 = 5
D (A,B)
E
c(E,B) + min {D (A,w)}
B
w
=
=
8+6 = 14
loop!
loop!

## Slide 17: Distance table gives routing table
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
A
B
C
D
A,1
D,5
D,4
D,4
Outgoing link
to use, cost
destination
Distance table
Routing table

## Slide 18: Distance Vector Routing: overview
Iterative, asynchronous: each local iteration caused by:
local link cost change
message from neighbor: its least cost path change from neighbor
Distributed:
each node notifies neighbors only when its least cost path to any destination changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost of msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:

## Slide 19: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 20: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent each
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n**2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network
Intra-AS and Inter-AS routing

## Slide 21: Hierarchical Routing
scale: with 50 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 22: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocols
  routers in different AS can run different intra-AS routing protocol
special routers in AS
run intra-AS routing protocol with all other routers in AS
also responsible for routing to destinations outside AS
  run inter-AS routing protocol with other gateway routers
gateway routers