## Slide 1: IPv6
Initial motivation: 32-bit address space completely allocated by 2008.
Additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
  new “anycast” address: route to “best” of several replicated servers
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 2: IPv6 Header (Cont)
Priority: identify priority among datagrams in flow
Flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
Next header: identify upper layer protocol for data

## Slide 3: Other Changes from IPv4
Checksum: removed entirely to reduce processing time at each hop
Options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 4: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operate with mixed IPv4 and IPv6 routers?
Two proposed approaches:
  Dual Stack: some routers with dual stack (v6, v4) can “translate” between formats
  Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers

## Slide 5: Dual Stack Approach

## Slide 6: Tunneling
IPv6 inside IPv4 where needed

## Slide 7: Multicast
Up to now we have seen protocols dealing with one single sender and one single receiver:
unicast
Some applications need that one or more senders communicate with a group of receivers
(teleconference, automatic software update…):
multicast

## Slide 8: How can we do it?
Implicit mode : n unicast connections
Explicit mode: a single datagram sent is replicated by routers

## Slide 9: Multicast Addressing
Multicast addr. uses class D addresses
Every host has an unique unicast address
Internet Group Management Protocol (IGMP) manages the communication of a single host linked to a router with multicast addressing
Multicast routers coordination needs a network-layer protocol for multicast routing algorithm
multicast group
226.17.30.197