## Slide 1: Introduction
Goal:
get context, overview, “feel” of networking
more depth, detail later in course
approach:
  descriptive
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
protocol layers, service models
history
ATM network

## Slide 2: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts, end-systems
  pc’s workstations, servers
  phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
routers: forward packets (chunks) of data thru network
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 3: What’s the Internet: “nuts and bolts” view
protocols: control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 4: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  WWW, email, games, e-commerce, database., voting,
  more?
communication services provided:
  connectionless
  connection-oriented
cyberspace [Gibson]:
  “a consensual hallucination experienced daily by billions of operators, in every nation, ...."

## Slide 5: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 6: What’s a protocol?
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://gaia.cs.umass.edu/index.htm
<file>
time

## Slide 7: A closer look at network structure:
network edge: applications and hosts
network core:
  routers
  network of networks
access networks, physical media: communication links

## Slide 8: The network edge:
end systems (hosts):
  run application programs
  e.g., WWW, email
  at “edge of network”
client/server model
  client host requests, receives service from server
  e.g., WWW client (browser)/ server; email client/server
peer-peer model:
  host interaction symmetric
  e.g.: teleconferencing

## Slide 9: Network edge: connection-oriented service
Goal: data transfer between end sys.
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 10: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (WWW), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, Internet telephony

## Slide 11: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 12: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 13: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 14: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed,
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  transmit over link
  wait turn at next link
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 15: Network Core: Packet Switching
Packet-switching versus circuit switching: human restaurant analogy
other human analogies?
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 16: Network Core: Packet Switching
Packet-switching:
store and forward behavior

## Slide 17: Packet switching versus circuit switching
1 Mbit link
each user:
  100Kbps when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less that .004
Packet switching allows more users to use network!
N users
1 Mbps link

## Slide 18: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 6)
Is packet switching a “slam dunk winner?”

## Slide 19: Packet-switched networks: routing
Goal: move packets among routers from source to destination
  we’ll study several path selection algorithms (chapter 4)
datagram network:
  destination address determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 20: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 21: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (conceptually)
ISDN: intergrated services digital network: 128Kbps all-digital connect to router
ADSL: asymmetric digital subscriber line
  up to 1 Mbps home-to-router
  up to 8 Mbps router-to-home

## Slide 22: Residential access: cable modems non diffuso in italia
HFC: hybrid fiber coax
  asymmetric: up to 10Mbps upstream, 1 Mbps downstream
network of cable and fiber attaches homes to ISP router
  shared access to router among home
  issues: congestion, dimensioning
deployment: available via cable companies, e.g., MediaOne

## Slide 23: Institutional access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated cable connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs soon
LANs: chapter 5

## Slide 24: Wireless access networks
shared wireless access network connects end system to router
wireless LANs:
  radio spectrum replaces wire
  e.g., Lucent Wavelan 10 Mbps
wider-area wireless access
  CDPD: wireless access to ISP router via cellular network
base
station
mobile
hosts
router

## Slide 25: Physical Media
physical link: transmitted data bit propagates across link
guided media:
  signals propagate in solid media: copper, fiber
unguided media:
  signals propagate freelye.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps ethernet
  Category 5 TP: 100Mbps ethernet

## Slide 26: Physical Media: coax, fiber
Coaxial cable:
wire (signal carrier) within a wire (shield)
  baseband: single channel on cable
  broadband: multiple channel on cable
bidirectional
common use in 10Mbs Ethernet
Fiber optic cable:
glass fiber carrying light pulses
high-speed operation:
  100Mbps Ethernet
  high-speed point-to-point transmission (e.g., 5 Gps)
low error rate

## Slide 27: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
microwave
  e.g. up to 45 Mbps channels
LAN (e.g., waveLAN)
  2Mbps, 11Mbps
wide-area (e.g., cellular)
  e.g. CDPD(Cellular Digital Packet Data) 10’s kbps
satellite
  up to 50Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus LEOS

## Slide 28: Delay in packet-switched networks
packets experience delay on end-to-end path
four sources of delay at each hop
nodal processing:
  check bit errors
  determine output link
queueing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing

## Slide 29: Delay in packet-switched networks
Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantitites!

## Slide 30: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 31: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 32: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 33: Organization of air travel: a different view
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 34: Layered air travel: services
Counter-to-counter delivery of person+bags
baggage-claim-to-baggage-claim delivery
people transfer: loading gate to arrival gate
runway-to-runway delivery of plane
airplane routing from source to destination

## Slide 35: Distributed implementation of layer functionality
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departing airport
arriving airport
intermediate air traffic sites
airplane routing
airplane routing

## Slide 36: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 37: Internet protocol stack
application: supporting network applications
  ftp, smtp, http
transport: host-host data transfer
  tcp, udp
network: routing of datagrams from source to destination
  ip, routing protocols
link: data transfer between neighboring network elements
  ppp, ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 38: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 39: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 40: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 41: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 42: Internet structure: network of networks
roughly hierarchical
national/international backbone providers (NBPs)
  e.g. BBN/GTE, Sprint, AT&T, IBM, UUNet
  interconnect (peer) with each other privately, or at public Network Access Point (NAPs)
regional ISPs
  connect into NBPs
local ISP, company
  connect into regional ISPs
NBP A
NBP B
NAP
NAP
regional ISP
regional ISP
local
ISP
local
ISP

## Slide 43: National Backbone Provider
e.g. BBN/GTE US backbone network

## Slide 44: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Reearch Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 45: Internet History
1970: ALOHAnet satellite network in Hawaii
1973: Metcalfe’s PhD thesis proposes Ethernet
1974: Cerf and Kahn - architecture for interconnecting networks
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 46: Internet History
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 47: Internet History
Early 1990’s: ARPAnet decomissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: WWW
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, http: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the WWW
Late 1990’s:
est. 50 million computers on Internet
est. 100 million+ users
backbone links runnning at 1 Gbps
1990’s: commercialization, the WWW

## Slide 48: ATM: Asynchronous Transfer Mode nets
Internet:
today’s de facto standard for global data networking
1980’s:
telco’s develop ATM: competing network standard for carrying high-speed voice/data
standards bodies:
  ATM Forum
  ITU
ATM principles:
small (48 byte payload, 5 byte header) fixed length cells (like packets)
  fast switching
  small size good for voice
virtual-circuit network: switches maintain state for each “call”
well-defined interface between “network” and “user” (think of telephone company)

## Slide 49: ATM layers
ATM Adaptation Layer (AAL): interface to upper layers
  end-system
  segmentation/reassembly
ATM Layer: cell switching
Physical
AAL
ATM
physical
AAL
ATM
physical
AAL
ATM
physical
AAL
ATM
physical
ATM
physical
Where’s the application?
ATM: lower layer
functionality only
IP-over ATM: later
application
TCP/UDP
IP
application
TCP/UDP
IP
application
TCP/UDP
IP
application
TCP/UDP
IP

## Slide 50: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
performance: loss, delay
layering and service models
backbones, NAPs, ISPs
history
ATM network
You now hopefully have:
context, overview, “feel” of networking
more depth, detail later in course

## Slide 51: Application Layer
Goals:
conceptual + implementation aspects of network application protocols
  client server paradigm
  service models
learn about protocols by examining popular application-level protocols
More goals
specific protocols:
  http (HyperText Transfer Protocol)
  ftp (File Transfer Protocol)
  Smtp (Simple MailTransfer Protocol)
  pop (Post Office Protocol)
  dns (Domain Name System)
programming network applications
  socket programming

## Slide 52: Applications and application-layer protocols
Application: communicating, distributed processes
  running in network hosts in “user space”
  exchange messages to implement app
  e.g., email, file transfer, the Web
Application-layer protocols
  one “piece” of an app
  define messages exchanged by apps and actions taken
  user services provided by lower layer protocols
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 53: Network applications: some jargon
A process is a program that is running within a host.
Within the same host, two processes communicate with interprocess communication defined by the OS.
Processes running in different hosts communicate with an application-layer protocol
A user agent is an interface between the user and the network application.
  Web:browser
  E-mail: mail reader
  streaming audio/video: media player

## Slide 54: Client-server paradigm
Typical network app has two pieces: client and server
application
transport
network
data link
physical
application
transport
network
data link
physical
Client:
initiates contact with server (“speaks first”)
typically requests service from server,
for Web, client is implemented in browser; for e-mail, in mail reader
Server:
provides requested service to client
e.g., Web server sends requested Web page, mail server delivers e-mail
request
reply

## Slide 55: Application-layer protocols
API: application programming interface
defines interface between application and transport layer
socket: Internet API
  two processes communicate by sending data into socket, reading data out of socket
Q: how does a process “identify” the other process with which it wants to communicate?
  IP address of host running other process
  “port number” - allows receiving host to determine to which local process the message should be delivered
  Transport service requirements of common appsInternet apps: their protocols and transport protocol
… lots more on this later.