## Slide 1: Introduction
Goal:
get context, overview, “feel” of networking
more depth, detail later in course
approach:
  descriptive
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
protocol layers, service models
history
ATM network

## Slide 2: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts, end-systems
  pc’s workstations, servers
  phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
routers: forward packets (chunks) of data thru network
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 3: What’s the Internet: “nuts and bolts” view
protocols: control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 4: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  WWW, email, games, e-commerce, database., voting,
  more?
communication services provided:
  connectionless
  connection-oriented
cyberspace [Gibson]:
  “a consensual hallucination experienced daily by billions of operators, in every nation, ...."

## Slide 5: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 6: What’s a protocol?
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://gaia.cs.umass.edu/index.htm
<file>
time

## Slide 7: A closer look at network structure:
network edge: applications and hosts
network core:
  routers
  network of networks
access networks, physical media: communication links

## Slide 8: The network edge:
end systems (hosts):
  run application programs
  e.g., WWW, email
  at “edge of network”
client/server model
  client host requests, receives service from server
  e.g., WWW client (browser)/ server; email client/server
peer-peer model:
  host interaction symmetric
  e.g.: teleconferencing

## Slide 9: Network edge: connection-oriented service
Goal: data transfer between end sys.
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 10: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (WWW), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, Internet telephony

## Slide 11: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 12: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 13: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 14: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed,
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  transmit over link
  wait turn at next link
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 15: Network Core: Packet Switching
Packet-switching versus circuit switching: human restaurant analogy
other human analogies?
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 16: Network Core: Packet Switching
Packet-switching:
store and forward behavior

## Slide 17: Packet switching versus circuit switching
1 Mbit link
each user:
  100Kbps when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less that .004
Packet switching allows more users to use network!
N users
1 Mbps link

## Slide 18: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 6)
Is packet switching a “slam dunk winner?”

## Slide 19: Packet-switched networks: routing
Goal: move packets among routers from source to destination
  we’ll study several path selection algorithms (chapter 4)
datagram network:
  destination address determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 20: Access networks and physical media
Q: How to connection end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 21: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (conceptually)
ISDN: intergrated services digital network: 128Kbps all-digital connect to router
ADSL: asymmetric digital subscriber line
  up to 1 Mbps home-to-router
  up to 8 Mbps router-to-home

## Slide 22: Residential access: cable modems non diffuso in italia
HFC: hybrid fiber coax
  asymmetric: up to 10Mbps upstream, 1 Mbps downstream
network of cable and fiber attaches homes to ISP router
  shared access to router among home
  issues: congestion, dimensioning
deployment: available via cable companies, e.g., MediaOne

## Slide 23: Institutional access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated cable connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs soon
LANs: chapter 5

## Slide 24: Wireless access networks
shared wireless access network connects end system to router
wireless LANs:
  radio spectrum replaces wire
  e.g., Lucent Wavelan 10 Mbps
wider-area wireless access
  CDPD: wireless access to ISP router via cellular network
base
station
mobile
hosts
router