## Slide 1: LAN technologies
Data link layer so far:
  services, error detection/correction, multiple access
Next: LAN technologies
  addressing
  Ethernet
  hubs, bridges, switches
  802.11
  PPP
  ATM

## Slide 2: LAN Addresses and ARP
32-bit IP address:
network-layer address
used to get datagram to destination network (recall IP network definition)
LAN (or MAC or physical) address:
used to get frame from one interface to another physically-connected interface (same network)
48 bit MAC address (for most LANs) burned in the adapter ROM

## Slide 3: LAN Addresses and ARP
Each adapter on LAN has unique LAN address

## Slide 4: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address => portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on network to which one attaches

## Slide 5: Recall earlier routing discussion
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B, find B on same net. as A
link layer send datagram to B inside link-layer frame
B’s MAC
addr
A’s MAC
addr
A’s IP
addr
B’s IP
addr
IP payload
datagram
frame
frame source,
dest address
datagram source,
dest address

## Slide 6: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP module, table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
< ………………………….. >
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
given B’s IP address?

## Slide 7: ARP protocol
A knows B's IP address, wants to learn physical address of B
A broadcasts ARP query pkt, containing B's IP address
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) physical layer address
A caches (saves) IP-to-physical address pairs until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed

## Slide 8: Routing to another LAN
walkthrough: routing from A to B via R
In routing table at source Host, find router 111.111.111.110
In ARP table at source, find MAC address E6-E9-00-17-BB-4B, etc
A
R
B

## Slide 9
A creates IP packet with source A, destination B
A uses ARP to get R’s physical layer address for 111.111.111.110
A creates Ethernet frame with R's physical address as dest, Ethernet frame contains A-to-B IP datagram
A’s data link layer sends Ethernet frame
R’s data link layer receives Ethernet frame
R removes IP datagram from Ethernet frame, sees its destined to B
R uses ARP to get B’s physical layer address
R creates frame containing A-to-B IP datagram sends to B
A
R
B

## Slide 10: Ethernet
“dominant” LAN technology:
cheap $20 for 100Mbs!
first widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10, 100, 1000 Mbps
Metcalfe’s Etheret
sketch

## Slide 11: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
  7 bytes with pattern 10101010 followed by one byte with pattern 10101011
  used to synchronize receiver, sender clock rates
Data : 46 to 1500 byte

## Slide 12: Ethernet Frame Structure (more)
Addresses: 6 bytes, frame is received by all adapters on a LAN and dropped if address does not match
Type: indicates the higher layer protocol, mostly IP but others may be supported such as Novell IPX and AppleTalk)
CRC: checked at receiver, if error is detected, the frame is simply dropped

## Slide 13: Ethernet: uses CSMA/CD
A: sense channel, if idle
  then {
  transmit and monitor the channel;
      If detect another transmission
      then {
      abort and send jam signal;
        update # collisions;
        delay as required by exponential backoff algorithm;
        goto A
        }
      else {done with the frame; set collisions to zero}
    }
  else {wait until ongoing transmission is over and goto A}

## Slide 14: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits;
Exponential Backoff:
Goal: adapt retransmission attemtps to estimated current load
  heavy load: random wait will be longer
first collision: choose K from {0,1}; delay is K x 512 bit transmission times (0.01 microsec at 100 Mbps)
after second collision: choose K from {0,1,2,3}…
after ten or more collisions, choose K from {0,1,2,3,4,…,1023}

## Slide 15: Ethernet Technologies: 10Base2
10: 10Mbps; 2: under 200 meters max cable length
thin coaxial cable in a bus topology
repeaters used to connect up to multiple segments
repeater repeats bits it hears on one interface to its other interfaces: physical layer device only!

## Slide 16: 10BaseT and 100BaseT
10/100 Mbps rate; latter called “fast ethernet”
T stands for Twisted Pair
Hub to which nodes are connected by twisted pair, thus “star topology”
CSMA/CD implemented at hub

## Slide 17: 10BaseT and 100BaseT (more)
Max distance from node to Hub is 100 meters
Hub can disconnect “jabbering” adapter
Hub can gather monitoring information, statistics for display to LAN administrators

## Slide 18: Gbit Ethernet
uses standard Ethernet frame format
allows for point-to-point links and shared broadcast channels
in shared mode, CSMA/CD is used; short distances between nodes to be efficient
uses hubs, called here “Buffered Distributors”
Full-Duplex at 1 Gbps for point-to-point links

## Slide 19: Token Passing: IEEE802.5 standard
4 Mbps
max token holding time: 10 ms, limiting frame length
SD, ED mark start, end of packet
AC: access control byte:
  token bit: value 0 means token can be seized, value 1 means data follows FC
  priority bits: priority of packet
  reservation bits: station can write these bits to prevent stations with lower priority packet from seizing token after token becomes free

## Slide 20: Token Passing: IEEE802.5 standard
FC: frame control used for monitoring and maintenance
source, destination address: 48 bit physical address, as in Ethernet
data: packet from network layer
checksum: CRC
FS: frame status: set by dest., read by sender
  set to indicate destination up, frame copied OK from ring
  DLC-level ACKing

## Slide 21: Interconnecting LANs
Q: Why not just one big LAN?
Limited amount of supportable traffic: on single LAN, all stations must share bandwidth
limited length: 802.3 specifies maximum cable length
large “collision domain” (can collide with many stations)
limited number of stations: 802.5 have token passing delays at each station

## Slide 22: Hubs
Physical Layer devices: essentially repeaters operating at bit levels: repeat received bits on one interface to all other interfaces
Hubs can be arranged in a hierarchy (or multi-tier design), with backbone hub at its top

## Slide 23: Hubs (more)
Each connected LAN referred to as LAN segment
Hubs do not isolate collision domains: node may collide with any node residing at any segment in LAN
Hub Advantages:
  simple, inexpensive device
  Multi-tier provides graceful degradation: portions of the LAN continue to operate if one hub malfunctions
  extends maximum distance between node pairs (100m per Hub)

## Slide 24: Hub limitations
single collision domain results in no increase in max throughput
  multi-tier throughput same as single segment throughput
individual LAN restrictions pose limits on number of nodes in same collision domain and on total allowed geographical coverage
cannot connect different Ethernet types (e.g., 10BaseT and 100baseT)

## Slide 25: Bridges
Link Layer devices: operate on Ethernet frames, examining frame header and selectively forwarding frame based on its destination
Bridge isolates collision domains since it buffers frames
When frame is to be forwarded on segment, bridge uses CSMA/CD to access segment and transmit

## Slide 26: Bridges (more)
Bridge advantages:
  Isolates collision domains resulting in higher total max throughput, and does not limit the number of nodes nor geographical coverage
  Can connect different type Ethernet (or other ) since it is a store and forward device
  Transparent: no need for any change to hosts LAN adapters

## Slide 27: Bridges: frame filtering, forwarding
bridges filter packets
  same-LAN -segment frames not forwarded onto other LAN segments
forwarding:
  how to know which LAN segment on which to forward frame?
  looks like a routing problem (more shortly!)

## Slide 28: Backbone Bridge

## Slide 29: Interconnection Without Backbone
Not recommended for two reasons:
  - single point of failure at Computer Science hub
  - all traffic between EE and SE must path over CS segment

## Slide 30: Bridges Spanning Tree
for increased reliability, desirable to have redundant, alternate paths from source to dest
with multiple simultaneous paths, cycles result - bridges may multiply and forward frame forever
solution: organize bridges in a spanning tree by disabling subset of interfaces
Disabled

## Slide 31: Bridges vs. Routers
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  bridges are Link Layer devices
routers maintain routing tables, implement routing algorithms
bridges maintain filtering tables, implement filtering, learning and spanning tree algorithms

## Slide 32: Routers vs. Bridges
Bridges + and -
+ Bridge operation is simpler requiring less processing bandwidth
- Topologies are restricted with bridges: a spanning tree must be built to avoid cycles
- Bridges do not offer protection from broadcast storms (endless broadcasting by a host will be forwarded by a bridge)

## Slide 33: Routers vs. Bridges
Routers + and -
+ arbitrary topologies can be supported, cycling is limited by TTL counters (and good routing protocols)
+ provide firewall protection against broadcast storms
- require IP address configuration (not plug and play)
- require higher processing bandwidth
bridges do well in small (few hundred hosts) while routers used in large networks (thousands of hosts)

## Slide 34: Ethernet Switches
layer 2 (frame) forwarding, filtering using LAN addresses
Switching: A-to-B and A’-to-B’ simultaneously, no collisions
large number of interfaces
often: individual hosts, star-connected into switch
  Ethernet, but no collisions!

## Slide 35: Ethernet Switches
cut-through switching: frame forwarded from input to output port without awaiting for assembly of entire frame
  slight reduction in latency
combinations of shared/dedicated, 10/100/1000 Mbps interfaces

## Slide 36: Ethernet Switches (more)
Dedicated
Shared

## Slide 37: IEEE 802.11 Wireless LAN
wireless LANs: untethered (often mobile) networking
IEEE 802.11 standard:
  MAC protocol
  unlicensed frequency spectrum: 900Mhz, 2.4Ghz
BSS’s combined to form distribution system (DS)
Basic Service Set (BSS) (a.k.a. “cell”) contains:
  wireless hosts
  access point (AP): base station

## Slide 38: Ad Hoc Networks
Ad hoc network: IEEE 802.11 stations can dynamically form network without AP
Applications:
  “laptop” meeting in conference room, car
  interconnection of “personal” devices
IETF MANET (Mobile Ad hoc Networks) working group

## Slide 39: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 CSMA: sender
- if sense channel idle for DIFS (Distr. Inter Frame Space) sec.
then transmit entire frame (no collision detection)
-if sense channel busy then binary backoff
802.11 CSMA receiver:
if received OK
return ACK after SIFS (Short Inter Frame Spacing)

## Slide 40: IEEE 802.11 MAC Protocol
802.11 CSMA Protocol: others
NAV: Network Allocation Vector
802.11 frame has transmission time field
others (hearing data) defer access for NAV time units

## Slide 41: Hidden Terminal effect
hidden terminals: A, C cannot hear each other
  obstacles, signal attenuation
  collisions at B
goal: avoid collisions at B
CSMA/CA: CSMA with Collision Avoidance

## Slide 42: Collision Avoidance: RTS-CTS exchange
CSMA/CA: explicit channel reservation
  sender: send short RTS: request to send
  receiver: reply with short CTS: clear to send
CTS reserves channel for sender, notifying (possibly hidden) stations
avoid hidden station collisions

## Slide 43: Collision Avoidance: RTS-CTS exchange
RTS and CTS short:
  collisions less likely, of shorter duration
  end result similar to collision detection
IEEE 802.11 allows:
  CSMA
  CSMA/CA: reservations
  polling from AP

## Slide 44: Point to Point Data Link Control
one sender, one receiver, one link: easier than broadcast link:
  no Media Access Control
  no need for explicit MAC addressing
  e.g., dialup link, ISDN line
popular point-to-point DLC protocols:
  PPP (point-to-point protocol)
  HDLC: High level Data Link Control (Data link used to be considered “high layer” in protocol stack!

## Slide 45: PPP Design Requirements [RFC 1557]
packet framing: encapsulation of network-layer datagram in data link frame
  carry network layer data of any network layer protocol (not just IP) at same time
  ability to demultiplex upwards
bit transparency: must carry any bit pattern in the data field
error detection (no correction)
connection livenes: detect, signal link failure to network layer
network layer address negotiation: endpoint can learn/configure each other’s network address

## Slide 46: PPP non-requirements
no error correction/recovery
no flow control
out of order delivery OK
no need to support multipoint links (e.g., polling)
Error recovery, flow control, data re-ordering
all relegated to higher layers!|

## Slide 47: PPP Data Frame
Flag: delimiter (framing)
Address: does nothing (only one option)
Control: does nothing; in the future possible multiple control fields
Protocol: upper layer protocol to which frame delivered (eg, PPP-LCP, IP, IPCP, etc)

## Slide 48: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 49: Asynchronous Transfer Mode: ATM
1980s/1990’s standard for high-speed (155Mbps to 622 Mbps and higher) Broadband Integrated Service Digital Network architecture
Goal: integrated, end-end transport of carry voice, video, data
  meeting timing/QoS requirements of voice, video (versus Internet best-effort model)
  “next generation” telephony: technical roots in telephone world
  packet-switching (fixed length packets, called “cells”) using virtual circuits

## Slide 50: ATM architecture
adaptation layer: only at edge of ATM network
  data segmentation/reassembly
  roughly analagous to Internet transport layer
ATM layer: “network” layer
  cell switching, routing
physical layer

## Slide 51: ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  ATM is a network technology
Reality: used to connect IP backbone routers
  “IP over ATM”
  ATM as switched link layer, connecting IP routers

## Slide 52: ATM Adaptation Layer (AAL)
ATM Adaptation Layer (AAL): “adapts” upper layers (IP or native ATM applications) to ATM layer below
AAL present only in end systems, not in switches
AAL layer segment (header/trailer fields, data) fragmented across multiple ATM cells
  analogy: TCP segment in many IP packets

## Slide 53: ATM Adaption Layer (AAL) [more]
Different versions of AAL layers, depending on ATM service class:
AAL1: for CBR (Constant Bit Rate) services, e.g. circuit emulation
AAL2: for VBR (Variable Bit Rate) services, e.g., MPEG video
AAL5: for data (eg, IP datagrams)
AAL PDU
ATM cell
User data

## Slide 54: ATM Layer
Service: transport cells across ATM network
analagous to IP network layer
very different services than IP network layer
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 55: ATM Layer: Virtual Circuits
VC transport: cells carried on VC from source to dest
  call setup, teardown for each call before data can flow
  each packet carries VC identifier (not destination ID)
  every switch on source-dest path maintain “state” for each passing connection
  link,switch resources (bandwidth, buffers) may be allocated to VC: to get circuit-like perf.
Permanent VCs (PVCs)
  long lasting connections
  typically: “permanent” route between to IP routers
Switched VCs (SVC):
  dynamically set up on per-call basis

## Slide 56: ATM VCs
Advantages of ATM VC approach:
  QoS performance guarantee for connection mapped to VC (bandwidth, delay, delay jitter)
Drawbacks of ATM VC approach:
  Inefficient support of datagram traffic
  one PVC between each source/dest pair) does not scale (N*2 connections needed)
  SVC introduces call setup latency, processing overhead for short lived connections

## Slide 57: ATM Layer: ATM cell
5-byte ATM cell header
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
Cell header
Cell format

## Slide 58: ATM cell header
VCI: virtual channel ID
  will change from link to link thru net
PT: Payload type (e.g. RM cell versus data cell)
CLP: Cell Loss Priority bit
  CLP = 1 implies low priority cell, can be discarded if congestion
HEC: Header Error Checksum
  cyclic redundancy check

## Slide 59: ATM Physical Layer (more)
Two pieces (sublayers) of physical layer:
Transmission Convergence Sublayer (TCS): adapts ATM layer above to PMD sublayer below
Physical Medium Dependent: depends on physical medium being used
TCS Functions:
  Header checksum generation: 8 bits CRC
  Cell delineation
  With “unstructured” PMD sublayer, transmission of idle cells when no data cells to send

## Slide 60: ATM Physical Layer
Physical Medium Dependent (PMD) sublayer
SONET/SDH: transmission frame structure (like a container carrying bits);
  bit synchronization;
  bandwidth partitions (TDM);
  several speeds: OC1 = 51.84 Mbps; OC3 = 155.52 Mbps; OC12 = 622.08 Mbps
TI/T3: transmission frame structure (old telephone hierarchy): 1.5 Mbps/ 45 Mbps
unstructured: just cells (busy/idle)

## Slide 61: IP-Over-ATM
Classic IP only
3 “networks” (e.g., LAN segments)
MAC (802.3) and IP addresses
IP over ATM
replace “network” (e.g., LAN segment) with ATM network
ATM addresses, IP addresses
ATM
network
Ethernet
LANs
Ethernet
LANs

## Slide 62: IP-Over-ATM
Issues:
IP datagrams into ATM AAL5 PDUs
from IP addresses to ATM addresses
  just like IP addresses to 802.3 MAC addresses!
ATM
network
Ethernet
LANs

## Slide 63: Datagram Journey in IP-over-ATM Network
at Source Host:
  IP layer finds mapping between IP, ATM dest address (using ARP)
  passes datagram to AAL5
  AAL5 encapsulates data, segments to cells, passes to ATM layer
ATM network: moves cell along VC to destination
at Destination Host:
  AAL5 reassembles cells into original datagram
  if CRC OK, datgram is passed to IP

## Slide 64: ARP in ATM Nets
ATM network needs destination ATM address
  just like Ethernet needs destination Ethernet address
IP/ATM address translation done by ATM ARP (Address Resolution Protocol)
  ARP server in ATM network performs broadcast of ATM ARP translation request to all connected ATM devices
  hosts can register their ATM addresses with server to avoid lookup

## Slide 65: X.25 and Frame Relay
Like ATM:
wide area network technologies
virtual circuit oriented
origins in telephony world
can be used to carry IP datagrams
  can thus be viewed as Link Layers by IP protocol

## Slide 66: X.25
X.25 builds VC between source and destination for each user connection
Per-hop control along path
  error control (with retransmissions) on each hop
    variant of the HDLC protocol
  per-hop flow control using credits
    congestion arising at intermediate node propagates to previous node on path
    back to source via back pressure

## Slide 67: IP versus X.25
X.25: reliable in-sequence end-end delivery from end-to-end
  “intelligence in the network”
IP: unreliable, out-of-sequence end-end delivery
  “intelligence in the endpoints”
gigabit routers: limited processing possible
2000: IP wins

## Slide 68: Frame Relay
Designed in late ‘80s, widely deployed in the ‘90s
Frame relay service:
  no error control
  end-to-end congestion control

## Slide 69: Frame Relay (more)
Designed to interconnect corporate customer LANs
  typically permanent VC’s: “pipe” carrying aggregate traffic between two routers
  switched VC’s: as in ATM
corporate customer leases FR service from public Frame Relay network (eg, Telecom,Sprint, ATT)

## Slide 70: Frame Relay -VC Rate Control
Committed Information Rate (CIR)
  defined, “guaranteed” for each VC
  negotiated at VC set up time
  customer pays based on CIR
DE bit: Discard Eligibility bit
  Edge FR switch measures traffic rate for each VC; marks DE bit
  DE = 0: high priority, rate compliant frame; deliver at “all costs”
  DE = 1: low priority, eligible for discard when congestion

## Slide 71: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing, ARP
various link layer technologies
  Ethernet
  hubs, bridges, switches
  IEEE 802.11 LANs
  PPP
  ATM
  X.25, Frame Relay
journey down the protocol stack now OVER!