## Slide 1: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 2: UDP: more
often used for streaming multimedia apps
  loss tolerant
  rate sensitive
other UDP uses (why?):
  DNS
reliable transfer over UDP: add reliability at application layer
  application-specific error recover!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 3: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonethless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 4: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 5: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 6: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 7: Rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel

## Slide 8: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  recall: UDP checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
  human scenarios using ACKs, NAKs?
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender

## Slide 9: rdt2.0: FSM specification
sender FSM
receiver FSM

## Slide 10: rdt2.0: in action (no errors)
sender FSM
receiver FSM

## Slide 11: rdt2.0: in action (error scenario)
sender FSM
receiver FSM

## Slide 12: rdt2.0 has a fatal flaw!
What happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
What to do?
sender ACKs/NAKs receiver’s ACK/NAK? What if sender ACK/NAK lost?
retransmit, but this might cause retransmission of correctly received pkt!
Handling duplicates:
sender adds sequence number to each pkt
sender retransmits current pkt if ACK/NAK garbled
receiver discards (doesn’t deliver up) duplicate pkt
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 13: rdt2.1: sender, handles garbled ACK/NAKs

## Slide 14: rdt2.1: receiver, handles garbled ACK/NAKs

## Slide 15: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 16: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt
sender
FSM
!

## Slide 17: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Q: how to deal with loss?
  sender waits until certain data or ACK lost, then retransmits
  yuck: drawbacks?
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 18: rdt3.0 sender

## Slide 19: rdt3.0 in action

## Slide 20: rdt3.0 in action

## Slide 21: Performance of rdt3.0
rdt3.0 works, but performance stinks
example: 1 Gbps link, 15 ms e-e prop. delay, 1KB packet:
T
transmit
=
8kb/pkt
10**9 b/sec
= 8 microsec
Utilization = U =
=
8 microsec
30.016 msec
fraction of time
sender busy sending
= 0.00015
  1KB pkt every 30 msec -> 33kB/sec throughput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 22: Pipelined protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols: go-Back-N, selective repeat