## Slide 1: TCP Flow Control
receiver: explicitly informs sender of (dynamically changing) amount of free buffer space
  RcvWindow field in TCP segment
sender: keeps the amount of transmitted, unACKed data less than most recently received RcvWindow
sender won’t overrun
receiver’s buffers by
transmitting too much,
too fast
flow control
receiver buffering
RcvBuffer = size of TCP Receive Buffer
RcvWindow = amount of spare room in Buffer

## Slide 2: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
longer than RTT
  note: RTT will vary
too short: premature timeout
  unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions, cumulatively ACKed segments
SampleRTT will vary, want estimated RTT “smoother”
  use several recent measurements, not just current SampleRTT

## Slide 3: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket("hostname","port number");
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();
Three way handshake:
Step 1: client end system sends TCP SYN control segment to server
  specifies initial seq #
Step 2: server end system receives SYN, replies with SYNACK control segment
  ACKs received SYN
  allocates buffers
  specifies server-> receiver initial seq. #

## Slide 4: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 5: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handly simultaneous FINs.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 6: TCP Connection Management (cont)
TCP client
lifecycle
TCP server
lifecycle

## Slide 7: Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 8: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
no retransmission
large delays when congested
maximum achievable throughput

## Slide 9: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of lost packet

## Slide 10: Causes/costs of congestion: scenario 2
always: (goodput)
“perfect” retransmission only when loss:
retransmission of delayed (not lost) packet makes larger (than perfect case) for same

in

out
=

in

out
>

in

out
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt

## Slide 11: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit

in
Q: what happens as and increase ?

in

## Slide 12: Causes/costs of congestion: scenario 3
Another “cost” of congestion:
when packet dropped, any upstream transmission capacity used for that packet was wasted!

## Slide 13: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at
Two broad approaches towards congestion control:

## Slide 14: Case study: ATM ABR congestion control
ABR: available bit rate:
“elastic service”
if sender’s path “underloaded”:
  sender should use available bandwidth
if sender’s path congested:
  sender throttled to minimum guaranteed rate
RM (resource management) cells:
sent by sender, interspersed with data cells
bits in RM cell set by switches (“network-assisted”)
  NI bit: no increase in rate (mild congestion)
  CI bit: congestion indication
RM cells returned to sender by receiver, with bits intact

## Slide 15: Case study: ATM ABR congestion control
two-byte ER (explicit rate) field in RM cell
  congested switch may lower ER value in cell
  sender’ send rate thus minimum supportable rate on path
EFCI (explicit Forward Congestion Indication) bit in data cells: set to 1 in congested switch
  if data cell preceding RM cell has EFCI set, sender sets CI bit in returned RM cell

## Slide 16: TCP Congestion Control
end-end control (no network assistance)
transmission rate limited by congestion window size, Congwin, over segments:
n segments, each with MSS bytes sent in one RTT:
throughput =
n * MSS
RTT
Bytes/sec
Congwin

## Slide 17: TCP congestion control:
two “phases”
  slow start
  congestion avoidance
important variables:
  Congwin
  threshold: defines threshold between two slow start phase, congestion control phase
“probing” for usable bandwidth:
  ideally: transmit as fast as possible (Congwin as large as possible) without loss
  increase Congwin until loss (congestion)
  loss: decrease Congwin, then begin probing (increasing) again

## Slide 18: TCP Slowstart
exponential increase (per RTT) in window size (not so slow!)
loss event: timeout (Tahoe TCP) and/or or three duplicate ACKs (Reno TCP)
initialize: Congwin = 1
for (each segment ACKed)
Congwin++
until (loss event OR
CongWin > threshold)
Slowstart algorithm
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 19: TCP Congestion Avoidance
/* slowstart is over */
/* Congwin > threshold */
Until (loss event) {
every w segments ACKed:
Congwin++
}
threshold = Congwin/2
Congwin = 1
perform slowstart
Congestion avoidance
1
1: TCP Reno skips slowstart (fast
recovery) after three duplicate ACKs

## Slide 20: TCP Fairness
Fairness goal: if N TCP sessions share same bottleneck link, each should get 1/N of link capacity
TCP congestion avoidance:
AIMD: additive increase, multiplicative decrease
  increase window by 1 per RTT
  decrease window by factor of 2 on loss event
AIMD
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2

## Slide 21: Why is TCP fair?
Two competing sessions:
Additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 22: TCP latency modeling
Q: How long does it take to receive an object from a Web server after sending a request (latency)?
TCP connection establishment
data transfer delay
Notation, assumptions:
Assume one link between client and server of rate R
Assume: fixed congestion window, W segments
S: MSS (bits)
O: object size (bits)
no retransmissions (no loss, no corruption)
Two cases to consider:
WS/R > RTT + S/R: ACK for first segment in window returns before window’s worth of data sent
WS/R < RTT + S/R: wait for ACK after sending window’s worth of data sent

## Slide 23: TCP latency Modeling
Case 1: latency = 2RTT + O/R
Case 2: latency = 2RTT + O/R
+ (K-1)[S/R + RTT - WS/R]
K:= O/WS

## Slide 24: TCP Latency Modeling: Slow Start
Now suppose window grows according to slow start.
Will show that the latency of one object of size O is:
where P is the number of times TCP stalls at server:
- where Q is the number of times the server would stall
if the object were of infinite size.
- and K is the number of windows that cover the object.

## Slide 25: TCP Latency Modeling: Slow Start (cont.)
Example:
O/S = 15 segments
K = 4 windows
Q = 2
P = min{K-1,Q} = 2
Server stalls P=2 times.

## Slide 26: TCP Latency Modeling: Slow Start (cont.)

## Slide 27: Transport: Summary
principles behind transport layer services:
  multiplexing/demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation and implementation in the Internet
  UDP
  TCP
Next:
leaving the network “edge” (application transport layer)
into the network “core”

## Slide 28: Network Layer
Chapter goals:
understand principles behind network layer services:
  routing (path selection)
  dealing with scale
  how a router works
  advanced topics: IPv6, multicast
instantiation and implementation in the Internet
Overview:
network layer services
routing principle: path selection
hierarchical routing
IP
Internet routing protocols reliable transfer
  intra-domain
  inter-domain
what’s inside a router?
IPv6
multicast routing

## Slide 29: Network layer functions
transport packet from sending to receiving hosts
network layer protocols in every host, router
three important functions:
path determination: route taken by packets from source to dest. Routing algorithms
switching: move packets from router’s input to appropriate router output
call setup: some network architectures require router call setup along path before data flows
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 30: Network service model
Q: What service model for “channel” transporting packets from sender to receiver?
guaranteed bandwidth?
preservation of inter-packet timing (no jitter)?
loss-free delivery?
in-order delivery?
congestion feedback to sender?
?
?
?
virtual circuit
or
datagram?
The most important
abstraction provided
by network layer:
service abstraction

## Slide 31: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host ID)
every router on source-dest path s maintain “state” for each passing connection
  transport-layer connection only involved two end systems
link, router resources (bandwidth, buffers) may be allocated to VC
  to get circuit-like perf.
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 32: Virtual circuits: signaling protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 33: Datagram networks: the Internet model
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets typically routed using destination host ID
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 34: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 35: Datagram or VC network: why?
Internet
data exchange among computers
  “elastic” service, no strict timing req.
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
many link types
  different characteristics
  uniform service difficult
ATM
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 36: Routing
Graph abstraction for routing algorithms:
graph nodes are routers
graph edges are physical links
  link cost: delay, $ cost, or congestion level
Goal: determine “good” path
(sequence of routers) thru
network from source to dest.
Routing protocol
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
“good” path:
  typically means minimum cost path
  other def’s possible

## Slide 37: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 38: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives routing table for that node
iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(i,j): link cost from node i to j. cost infinite if not direct neighbors
D(v): current value of cost of path from source to dest. V
p(v): predecessor node along path from source to v, that is next v
N: set of nodes whose least cost path definitively known

## Slide 39: Dijsktra’s Algorithm
1 Initialization:
2 N = {A}
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v)
6 else D(v) = infty
7
8 Loop
9 find w not in N such that D(w) is a minimum
10 add w to N
11 update D(v) for all v adjacent to w and not in N:
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N

## Slide 40: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
start N
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
2,A
2,A
D(C),p(C)
5,A
4,D
3,E
3,E
D(D),p(D)
1,A
D(E),p(E)
infinity
2,D
D(F),p(F)
infinity
infinity
4,E
4,E
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 41: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n*(n+1)/2 comparisons: O(n**2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
A
D
C
B
2+e
0
0
0
1+e
1
A
D
C
B
0
2+e
1+e
1
0
0
A
D
C
B
2+e
0
e
0
1+e
1
initially
… recompute
routing
… recompute
… recompute

## Slide 42: Distance Vector Routing Algorithm
iterative:
continues until no nodes exchange info.
self-terminating: no “signal” to stop
asynchronous:
nodes need not exchange info/iterate in lock step!
distributed:
each node communicates only with directly-attached neighbors
Distance Table data structure
each node has its own
row for each possible destination
column for each directly-attached neighbor to node
example: in node X, for dest. Y via neighbor Z:
D (Y,Z)
X
distance from X to
Y, via Z as next hop
c(X,Z) + min {D (Y,w)}
Z
w
=
=

## Slide 43: Distance Table: example
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
D (C,D)
E
c(E,D) + min {D (C,w)}
D
w
=
=
2+2 = 4
D (A,D)
E
c(E,D) + min {D (A,w)}
D
w
=
=
2+3 = 5
D (A,B)
E
c(E,B) + min {D (A,w)}
B
w
=
=
8+6 = 14
loop!
loop!

## Slide 44: Distance table gives routing table
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
A
B
C
D
A,1
D,5
D,4
D,4
Outgoing link
to use, cost
destination
Distance table
Routing table

## Slide 45: Distance Vector Routing: overview
Iterative, asynchronous: each local iteration caused by:
local link cost change
message from neighbor: its least cost path change from neighbor
Distributed:
each node notifies neighbors only when its least cost path to any destination changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost of msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:

## Slide 46: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 47: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent each
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n**2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network
Intra-AS and Inter-AS routing