## Slide 1
JLab12 (R.N. & R.L.: Marco Contalbrigo)
Nucleon structure and spin physics
Transverse momentum phenomena (TMDs) & 3D imaging
GPDs & EM Form Factors of the nucleon
M. Contalbrigo elected in the Chair line of the JLab User Organization
(1900 users from US and all over the World)
M. Contalbrigo PI of the CLAS12 RICH detector
M. Contalbrigo contact person for RGH group of experiment
with transversely polarized target
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 2
Jlab12 Italia (R.N. & R.L. M. Contalbrigo)
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 3
Neutron rich matter equation of state
Precise determination of the neutral weak form factor of 48Ca and 208Pb.
PREX and CREX have performed a precise determination of the neutron skin thickness of the 48Ca and 208Pb nuclei. They provides constraints on the density dependence of the symmetry energy of neutron rich nuclear matter and thus neutron stars.
Unprecedented constraints complementary to gravitational wave interferometry.
Nucleon structure and mechanical properties
First CLAS12 Measurement of DVCS Beam-Spin Asymmetries in the Extended Valence Region.
The first CLAS12 measurement of the DVCS beam-spin asymmetry off unpolarized proton targets, greatly extends the x and Q2 phase space beyond the existing data in the valence region with unprecedented statistical precision.
Unprecedent access to pressure and share forces within the nucleon.
CLAS12: PRL 130 (2023) 21, 211902
PREX: PRL 106 (2021) 172502
CREX: PRL 129 (2022) 042501
T.Sarkar++ [PRC 108 (2003) 3]
JLab Highlights
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 4
CLAS12 Experiment in Hall-B
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 5
CLAS12 Experiment in Hall-B
CLAS12 detector
Lumi up to
High polarized electron beams
H and D polarized target
Broad kinematic range
Very good PID
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 6
CLAS12 Experiment in Hall-B
CLAS12 detector
Lumi up to
High polarized electron beams
H and D polarized target
Broad kinematic range
Very good PID
Physics program:
Hadron spectroscopy
Nuclear effects in hadronization
Nucleon structure (TMDs, GPDs)
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 7
CLAS12 Experiment in Hall-B
FF
TMDs depend on and
Describe correlations between and quark or nucleon spin (spin-orbit correlations)
Provide a 3-dim picture of the nucleon in momentum space (nucleon tomography)
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 8
CLAS12 Experiment in Hall-B
FF
TMDs depend on and
Describe correlations between and quark or nucleon spin (spin-orbit correlations)
Provide a 3-dim picture of the nucleon in momentum space (nucleon tomography)
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 9
The RICH detector project (INFN)
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
George Washington University (USA)
Glasgow University (Glasgow, UK)
J. Gutenberg Universitat Mainz (Mainz, Germany)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
Completed with 2nd module in June 2022
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 10
The RICH Front-End electronics
FPGA Board (JLab)
ASIC Board (Ferrara)
Compact and modular electronics to readout multi-anode PMTs
Adopted by other experiments:
Gluex, SOLID, EIC R&D...
Adapted to different sensors:
Multi-anode PMT H12700, H13700
SiPM array S12642, H13361
Developed thanks to Roberto M., L. Barion
L. L. Pappalardo - C.d.S. INFN Ferrara – 04/07/2024

## Slide 11
The RICH Reconstruction
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
S. Vallarino PhD theis

## Slide 12
The Transverse target
superconducting
torus
superconducting
solenoid
target
polarized
e- beam
Internal Target
To maintain transverse spin polarization
within the CLAS12 solenoid and preserve wide acceptance for the final-state particles, new magnetic solutions are required.
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023

## Slide 13
Transverse Target:
high polarization
d 25 mm – Length 10 mm
transverse field up to 2 T
Tracking solenoid
design up to 5 T longitudinal
4K L-He cryostat
length 1500 mm
The Transverse target
superconducting
torus
superconducting
solenoid
target
polarized
e- beam
Internal Target
To maintain transverse spin polarization
within the CLAS12 solenoid and preserve wide acceptance for the final-state particles, new magnetic solutions are required.
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023

## Slide 14
magnetization
Transverse target: bulk transverse magnet
A hollow bulk superconductor is able to provide a transverse holding field inside, while adjusting its internal currents to shield any outside field, without the need of a current supply!
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Alternative to the use of a massive 5 T magnet to increase acceptance (for recoil)

## Slide 15
Transverse target: the new cryostat
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
New concept:
pre-conditioned bulk superconductor
- new cryostat
- new holder probe (6x)
- smart MgB2 sample exchange
Magnetization @ 1 T
Developed thanks to L. Barion, M. Cavallina

## Slide 16
Recoil Reconstruction
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Recoil concept
Simulated RGH recoil resolution
based on ongoing tech. development
and CLAS12 FD tracking resolution
CLAS12 Standard

## Slide 17
Sintillating Fiber Detector
Developed thanks to L. Barion, M. Roberto, M. Cavallina
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
New potential application of the CLAS12 RICH Electronics reading SiPM
To be used as fast beam particle tracking with RICH prototypes
Potential use as recoil detector for CLAS12 – RGH (transversely polarized targets)

## Slide 18
Sintillating Fiber Detector
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
x (mm)
y (mm)
GEM
chamber
Sci-Fi
detector
Beam profile

## Slide 19
Il gruppo di Ferrara @ JLab
Responsabilita’:
M. C.: responsabile locale e nazionale di JLab12 (till June ‘24)
M. C. : chair of the Jlab User Organization (till June ‘24)
M. C.: contact person for the RGH experiments with transversely polarized target
M. C. responsabile progetto RICH
M. C. & L.P. Co-spokesperson di diverse proposte di esperimento (PAC34,37,38,39)
Contributi principali del gruppo:
Data analysis
- Data analysis on kaon SIDIS
RICH detector
- Reconstruction and alignment algorithms
Magneti superconduttori
- Configurazione magnetica per transverse target
- Frozen field con magneti a bulk di superconduttore
- Recoil detector design
Esperimenti con bersagli trasversi
- Study scintillating-fiber (time) tagger
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023

## Slide 20
EIC-NET (R.L.: Marco Contalbrigo)
INFN Network for preliminary studies on the EIC project
M. Contalbrigo is dRICH detector subsystem lead
co-coordinator of the dRICH R&D EIC Program (eRD102)
A. Saputi is Contact Person for dRICH mechanics
dRICH: Dual-radiator RICH for the EIC hadron end-cap (project led by INFN)
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023

## Slide 21
EIC_NET
Electron Ion Collider:
Strong interest in Italian nuclear physics
community (theory and experiment)
CD1 approval in June 2021
EPIC Coll. for 1st detector start in fall 2022
Detector subsystems defined in spring 2023
pre-TDR expected at the end of 2024
CD2 & 3 expected in spring 2025
(start of construction)
INFN Ferrara leading the dRICH subsystem
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023

## Slide 22
EIC_NET: The dual RICH
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Compact cost-effective solution for particle identification in the high-energy endcap at EIC
CLAS12 RICH COMPASS RICH ALICE HMPID DARKSIDE ALCOR
Background Expertise:
e: 5 GeV to 18 GeV
p: 41 GeV, 100 to 275 GeV
p/A beam
e beam
BA, BO, CS, CT, FE ,
GE, LNS, RM1,
RM2, SA, TO, TS
EPIC
EIC RICH Consortium
…..
dRICH
…..

## Slide 23
EIC_NET: dRICH Organization Chart
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
6.10.04 Particle Identification Level-3
6.10.04.03 dRICH Level-4
CAM from DOE EIC Project
CAM from Project + DSTC from EPIC (M. Contalbrigo)
Photo-Detector Level-5
Work packages lead from EPIC
Front-end Asics Level-5
Data-acquisition Level-5
Mechanics Level-5
Gas radiator Level-5
Mirror Level-5
Aerogel Radiator Level-5
R. Preghenella, INFN-BO, INFN-FE, INFN-CS, INFN-SA, INFN-LNF, INFN-CT, NISER
F. Cossio, INFN-TO, INFN-BO
P. Antonioli, INFN-BO, INFN-FE
A. Saputi, INFN-FE, INFN-CT, INFN-GE, JLAB, BNL
F. Tessarotto, INFN-TS, BNL
A. Vossen, DUKE, INFN-FE
G. Volpe, INFN-BA, INFN-FE, RICH Consortium
INFN-TS, DUKE, INFN-FE
Simulation

## Slide 24
EIC_NET: Baseline Design
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
dRICH: cost-effective compact solution
Radiators: Aerogel (nAERO~1.02) + Gas (nC2F6 ~ 1.0008)
Detector: 0.5 m2/sector, 3x3 mm2 pixel  SiPM option
Main cover wide momentum range 3 - 50 GeV/c
features work in high (~ 1T) magnetic field
fit in a quite limited (for a gas RICH) space
ATHENA case
Essential for semi-inclusive physics
due to absence of kinematics constraints at event-level

## Slide 25
EIC_NET: Mechanics
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Windows: sandwich panel made of two ~1 mm carbon fiber reinforced epoxy skins separated by 30 mm PMI foam or Al honeycomb (~ 1% X0)
Shells: 3 mm (inner tube) to 8 mm (outer tube) thick carbon fiber epoxy composite (~ 4% X0)
Skins formed with two layers of balanced weave laminate with fibers at 0o/90o and +/- 45o for uniform stiffness
Design thanks to A. Saputi, L. Barion

## Slide 26
EIC_NET: SiPM
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
ePIC background group
beam-beam interactions only
1-MeV neutron equivalent fluence (1 fb-1 ep running)
Benchmark fluence (10 x)
~ 107 1-MeV neq/cm2 / fb-1
1.7 T field
Strong and not-uniform magnetic field
Moderate radiation levels (up tp 1011 neq/cm2)
Usage of SiPM with
- low temperature working point
- periodic annealing at high temperature
(in-site by Joule effect)
R. Preghenella, NIIMA 1046 (2023) 167661
dRICH
dRICH

## Slide 27
EIC_NET: Photo-Detector
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Photon Detector Unit (PDU):
Compact to minimize space
4x Hamamatsu S13361-3050HS SiPM arrays
4x Front-End Boards (FEB)
4x ALCOR chip (ToT discrimination)
1x Read-Out Board (RDO)
1x Cooling plate (< -30 C)
Active area is shaped to resemble the focal surface and best exploits the focalization.
Electronics is minimized to fit the limited available space.
Detector box:
Shaped to fit the space
Quartz window
Cooling for sensors and electronics
Power distributing patch panel
Heat insulation
Heat exchanger
Cold plate
SiPM array
Back-side
connectors
FEB
(ALCOR)
Service
connections
RDO
Flex PCB
SiPM array
ALCOR chip
12 cm

## Slide 28
EIC_NET: dRICH Prototype
GEM
GEM
MAPMTs
Aerogel
Gas Vessel
Operative prototype commissioned. Double ring imaging achieved. Performance in line
with expectations except for aerogel single-photon angular resolution (worse by a factor ~ 1.5)
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Realization thanks to L. Barion, M. Cavallina, R. Malaguti

## Slide 29
EIC_NET: dRICH Prototype Highlight
Realization of a suitable detector plane for the dRICH prototype (23/10): Design ready, procurement aligned to 2023 test-beam campaign.
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Realization thanks to L. Barion, M. Cavallina, R. Malaguti
Photon Detection Unit
Streaming readout mode
Readout Box
8 PDUs, 2048 channels
Prototype
Working Pooint -40:-20 C

## Slide 30
EIC_NET: dRICH Prototype Highlight
Realization of a suitable detector plane for the dRICH prototype (24/05): completed readout plane.
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Realization thanks to L. Barion, M. Cavallina, R. Malaguti
Photon Detection Unit Insertion

## Slide 31
EIC_NET: dRICH Prototype Highlight
Realization of a suitable detector plane for the dRICH prototype (24/05): completed readout plane.
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Realization thanks to L. Barion, M. Cavallina, R. Malaguti
Aerogel + C2F6 radiators, positve beam, 8 GeV/c
p
p
e
p
gas ring
as p veto

## Slide 32
EIC_NET: Induced Temperature Gradients
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Realization thanks to L. Barion
Temperature in the gas volume induced by the SiPM surface at -30o

## Slide 33
EIC_NET: dRICH Aerogel
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Aerogel Factory (BELLE-II)
Initial evaluation & Reproducibility
on small samples in sinergy with ALICE
CLAS12 RICH quality assurance laboratory @ INFN-FE being refurnished
Lab char.
Test-beam
Improving traparency
Realization thanks to L. Barion

## Slide 34
EIC_NET: dRICH Mirror
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
CMA Carbon fiber mirrors (HERMES, AMS, LHCb, CLAS12)
cost-effective light & stiff solution:
roughness driven by mandrel 1-2 nm rms
surface accuracy better than 0.2 mrad
radius reproducibility better than 1 %
CLAS12 RICH quality assurance laboratory @ JLab being
refurnished in collaboration with DUKE University
Mirror aberrations
Realization thanks to A. Saputi
Small demonstrator:
Mid-size demonstrator:

## Slide 35
EIC_NET: dRICH Prototype Milestones
2025: Real-scale prototype for TDR (1 sector)
Mechanical structure
Realistic optics (off-axis)
ALCOR64 FEB + RDO
Aerogel and mirror demonstrator
New EIC-driven readout unit
L. L. Pappalardo - C.d.S. INFN Ferrara – 05/07/2023
Realization thanks to L. Barion, M. Cavallina, R. Malaguti
2025++: Detector box
Mechanical structure
Quartz windows
Cooling
Thermal models

## Slide 36
Responsabilita’:
M. C.: responsabile locale EIC_NET
M. C.: responsabile dRICH
A. S.: contact for dRICH mechanics
M. C.: co-coordinator eRD102
M. C.: IAC POETIC (Physics Opportunities at EIC) Conference
Contributi principali:
dRICH detector
- dRICH mechanics
- Prototyping
- Optical component characterization
- SiPM irradiation program
Electronics
- MAROC (reference) + ALCOR (INFN development)
EIC_NET: responsabilità

## Slide 37
Richieste ai Servizi
Servizio Meccanico
FE laboratory: supporto per misure e stazioni di test, preparazione test-beam
JLAB12
TTarget: supporto per test con doppio campo magnetico al LASA di Milano
Recoil: contributo meccanica tracciatore recoil
EIC_NET
dRICH: progettazione meccanica del rivelatore dRICH
dRICH: meccanica del prototipo dRICH
Servizio Elettronico
FE laboratory: supporto per misure e stazioni di test, preparazione test-beam
JLAB12
TTarget: piccoli contributi alle misure con magneti superconduttori
TTarget: contributo per recoil detector (fibre scintillanti)
EIC_NET
dRICH: contributo piano di rivelazione curvo basato su SiPM + ALCOR
dRICH: master panel di controllo rivelatore

## Slide 38
Manpower e richieste finanziarie per 2025
Name | JEDI | JLab12 | EIC_NET
N. Canale (dottorando) | 100 |  | 
G. Ciullo (staff) | 70 | 20 | 
M. Contalbrigo (staff) |  | 50 | 50
S. Dymov (post-doc) | 100 |  | 
L. Del Bianco (staff) |  | 100 | 
A. Kononov (dottorando) | 100 |  | 
P. Lenisa (staff) | 75 | 20 | 
A. Maragno (dottoranda) | 100 |  | 
L. Pappalardo (RTD-B) |  | 30 | 
A. Pesce (post-doc) | 100 |  | 
A. Seleev (assegnista) | 100 |  | 
R. Shankar (dottorando) | 100 |  | 
F. Spizzo (staff) |  | 70 | 30
S. Plavully (assegnista) |  | 80 | 20
A. Saputi |  |  | 10
A. Cotta Ramusino (staff) | 10 |  | 
TOTALE/100 | 8.6 | 3.7 | 1.1
Name | JEDI | JLab12 | EIC_NET | Dot.3
Missioni | 57 | 45 | 25 | 8
Trasp. |  | 5 |  | 
Inv. | 9 |  |  | 15
Consumi | 34.5 | 15 | 40 | 6
Apparati |  | 10 |  | 
Altro |  |  |  | 3
TOTALE | 100.5 | 75 | 65 | 32
Richieste finanziarie (k€)
Name | JEDI | JLab12 | EIC_NET
L. Barion |  | 25 | 75
M. Cavallina | 10 | 10 | 
M. Gambetti | 10 |  | 
R. Malaguti |  | 20 | 
M. Melchiorri |  |  | 10
S. Squerzanti |  | 20 | 
TOTALE/100 | 0.2 | 0.5 | 0.1
Anagrafica e afferenze (Ric. + Tecnol.)
Servizio meccanico ed elettronico