## Slide 1
Italian Institutions at JLAB
INFN Bari, Uni & INFN Catania, Uni & INFN Ferrara, Uni & INFN Genova, INFN LNF,
Uni & INFN Padova, Uni Roma Sapienza & INFN Roma, Italian National Institute of Health ,
Uni & INFN Roma Tor Vergata, Uni Sassari & INFN Cagliari, INFN Torino
The Italian Contribution to the Thomas Jefferson National Accelerator Facility
An International Collaboration:
INFN (Italy), JLab (USA), ANL (USA) , Duquesne Univ. (USA) The George Washington Univ. (USA), Univ. of Connecticut (USA),
Kyungpook National Univ. (Republic of Korea), Univ. Tecnica Federico Santa Maria (Chile), Univ. of Glasgow (UK).
The Ring Imaging Cherenkov detector (RICH) is designed to improve the
CLAS12 Particle Identification (PID) in the momentum range 3-8 GeV/c
Kaon Identification
Aerogel Radiator
Complex Mirror System
Hybrid Geometry
Project status
1st module assembled in 2017
1s module installed in CLAS12 in January 2018
First Phase of Run Group-A data taking completed (Jan-May2018)
2nd module under constrution,
installation foreseen by 2020
MA-PMTs
Used to reduce the instrumented detection area
- 10 CFRP Spherical Mirrors (R=2.7 m) - 4 Frontal Planar Mirrors (glass-skin) - 7 Lateral Planar Mirrors (glass)
Front-End Electronics
Hamamatsu H12700 & H8500
Single Photon Sensitivity
Pixel size : 5.8 mm Packing Factor: 89% Maximum quantum efficiency: Visible light
First detector using H12700
THE CLAS12
MAROC3 readout chip:
DAQ Electronics:
FPGA serving group of 2/3 MAROCS
64 Channels
Digital readout
Single channel configurability
Innovative hybrid design to reduce cost and material budget
Angles: θ < 13° Momenta:3-8 GeV/c
Direct detection of Cherenkov light
Angles: Momenta:3-6 GeV/c
Reflection of Cherenkov Light
Multiple reflections. Double passage in aerogel.
13° < θ < 25°
Only option in this momentum range
- Large single brick area: 20cm x 20cm
- Refractive index: n=1.05 - Emitted Light : Visible & UV
Improving CLAS12 PID
TOF provides PID
up to 3 GeV/c
Threshold Cherenkov
Counters provide PID above 8 GeV/c
π/K production ≈ 10
π/K rejection power> 500
A good PID is required for 4 approved
experiments.
The RICH is necessary for
the PID in the momenta
range 3-8 GeV/c