## Slide 1
RICH Integration in CLAS12
Contalbrigo Marco
INFN Ferrara
Rich Technical Review, 5 September 2013

## Slide 2
RICH Project Goal
2
Contalbrigo M.
Rich Technical Review, 5th September 2013, JLab
1st sector ready by the end of 2016
Designed to fit into
the LTCC clearance
on the same joints of
the forward carriage
Notes: 9 vs 8

## Slide 3
PT distribution
3
Contalbrigo M.
RICH Project Goal
z distribution
Full momentum coverage from 3 up to 8 GeV/c
Pion rejection above 3 GeV/c
Proton rejection above 5 GeV/c
Angular coverage reaching
above 20 and up to 25 degrees
Contamination limited at the few % level
Pion rejection close to 500
Proton rejection close to 100
1
10-1
10-2
10-3
10-4
p mis-ID
90% kaon efficiency
n-sigma separation
0
1
2
3
4
5
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 4
Commissioning & Calibration
4
Contalbrigo M.
Use no-track events:
Internal trigger on SPE dark-counts for digital threshold setting
Random trigger for dark-count (no beam) and background (with beam) studies
Vary beam intensity for occupancy studies
Pedestal stability & Common noise studies with analog readout
Use Electron Tracks:
Mimic pion signal (almost saturated at 4-5 GeV/c)
Alignment (i.e. with drift-chambers and among mirrors)
Aerogel refractive index map
Mirror aberration corrections
Tune of the pattern-recognition and reconstruction algorithms
Efficiency and mis-identification probability
Use meson and hyperon decays to validate RICH performances:
KS for pions
f for kaons
L for protons
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 5
Operation
5
Contalbrigo M.
Gas system (standard solutions exist):
 Dry atmosphere for the hydrophilic aerogel preservation
 Slight overpressure to prevent contamination
Slow Control (part of the general CLAS12 design):
 HV and LV power supply monitor
 Gas monitor: temperature, pressure, humidity
 RICH stability monitor (i.e. on pedestals, occupancy,
basic signals like high-energy electrons )
Rich Technical Review, 5th September 2013, JLab
Notes: Capire se serve box sealed o no

## Slide 6
Interference with Other Detectors
6
Contalbrigo M.
RICH material budget:
✓ Just in front of FTOF wall:
multiple scattering spread << of the FTOF time resolution
~ 0.25 X0 from PMTs
and F-E Electronics
FTOF resolution limit
Rich Technical Review, 5th September 2013, JLab
~ 0.008 X0 from 20mm
CFRP mirrors
~ 0.01-0.04 X0 from
2-6 cm aerogel
~ 0.01 X0 from
CFRP+glass mirror
h
Notes: 9 vs 8

## Slide 7
Interference with Other Detectors
7
Contalbrigo M.
RICH material budget:
comparable with ~0.26 X0 of FTOF and much less than preshower ~5 X0
energy spread << 10%/√E sampling calorimeter resolution
~ 0.25 X0 from PMTs
and F-E Electronics
Rich Technical Review, 5th September 2013, JLab
~ 0.008 X0 from 20mm
CFRP mirrors
~ 0.01-0.04 X0 from
2-6 cm aerogel
~ 0.01 X0 from
CFRP+glass mirror
h
Notes: 9 vs 8

## Slide 8
8
Drift Chamber Occupancy
Contalbrigo M.
No target field
With target field
L = 1035 cm-2 s-1
DIS rate: 1-10 kHz
Severe Moeller background
- 10-100 k within 250 ns
- contained by central solenoid
- showering into long-range photons
Rich Technical Review, 5th September 2013, JLab
Notes: Add to access several combinations of GPDs
Sapere radiation lenght del NMR coil

## Slide 9
The RICH Background
9
Contalbrigo M.
Major source of backgrounds
Photons conversions into the aerogel
or in the PMT glass window
producing Cerenkov light
Rich Technical Review, 5th September 2013, JLab

## Slide 10
The RICH Occupancy @ L=1034
10
Contalbrigo M.
20 ns in-time window
Target transverse magnet torque
20 ns in-time window
+ H8500 Q.E.
Value used in the simulation
Correlation in space neglected
Studies done for the physics run with transverse target indicates the
Moeller background is under control up to the maximum luminosity
thanks to RICH position, segmentation and fast readout
Rich Technical Review, 5th September 2013, JLab

## Slide 11
RICH Reconstruction
11
Contalbrigo M.
Reconstruction algorithm on place
Ongoing: tuning of parameters to
optimize the performances
Verify and optimize the performances
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 12
The Likelihood Method
12
Contalbrigo M.
(the hypothesis that maximizes is assumed to be true)
is the probability of a hit given the kinematics of track t and hypothesis h
is the hit pattern from data
= 1 if the ith PMT is hit
= 0 if the ith PMT is not hit
is the probability of no hit
is the total number of expected PMT hits
is a background term (assumed to be 10-4, fine with Moeller prelim. studies)
Rich Technical Review, 5th September 2013, JLab

## Slide 13
Hit probability
Event
photon hits
Hadron expected
patterns (200 trials)
Direct
Reflected
Hit prob > 3 10-3
y (mm)
X (mm)
pion kaon proton
The RICH Reconstruction Algorithm
Contalbrigo M.
13
Standard techniques available but important to optimize:
Geometry together with Likelihood parameters
(background, time coincidence window, p.d.f precision)
1
0
Poor ID confidence Good
Control with
Goodness Estimator
Charged Hadron Multiplicity
Rich Technical Review, 5th September 2013, JLab

## Slide 14
Events in CLAS12
14
Contalbrigo M.
P = 6.3 GeV/c q = 6 degrees RQP = 0.59
Good ID thanks to high photon yield
RQP reflects close Cherenkov rings
LH tuning not optimized yet
Mirror
PMTs
pion kaon proton
Rich Technical Review, 5th September 2013, JLab
Corresponds to a 1:500
rejection factor
Notes: 9 vs 8

## Slide 15
Events in CLAS12
15
Contalbrigo M.
P = 3.7 GeV/c q = 22 degrees RQP = 0.98
Good ID thanks to separate patterns
Un-identifications reflect photon yield
LH tuning not optimized yet
Mirror
PMTs
pion kaon proton
Rich Technical Review, 5th September 2013, JLab
Out-bending particles
Notes: 9 vs 8

## Slide 16
Events in CLAS12
16
Contalbrigo M.
P = 3.7 GeV/c q = 22 degrees RQP = 0.98
Good ID thanks to separate patterns
Un-identifications reflect photon yield
LH tuning not optimized yet
Mirror
PMTs
pion kaon proton
Rich Technical Review, 5th September 2013, JLab
In-bending particles
Notes: 9 vs 8

## Slide 17
CLAS12 Combined PID
17
Contalbrigo M.
Pion contamination in the kaon sample for In-bending Particles
Even with a tuning not yet
optimized the pion
contamination is of
the order of 1%
SIDIS particle flux
within acceptance
pion >> kaon everywhere
TOF +HTCC pion rejection
for 90% kaon efficiency
pion >> kaon in a broad region
TOF+HTCC+RICH
pion rejection
Rich Technical Review, 5th September 2013, JLab
~1:1000 rejection
from x10 to ~1%
Notes: 9 vs 8

## Slide 18
CLAS12 Combined PID
18
Contalbrigo M.
Pion contamination in the kaon sample for Out-bending Particles
Rich Technical Review, 5th September 2013, JLab
~1:500 rejection
from x5 to ~1%
Notes: 9 vs 8

## Slide 19
PT distribution
19
Contalbrigo M.
RICH Requirements
z distribution
✔ Full momentum coverage
from 3 up to 8 GeV/c
Pion rejection above 3 GeV/c
Proton rejection above 5 GeV/c
Angular coverage reaching
✔ above 20 and
✔ up to 25 degrees
(optimization in progress)
✔ Contamination limited at the few % level
Pion rejection close to 500
Proton rejection close to 100
1
10-1
10-2
10-3
10-4
p mis-ID
90% kaon efficiency
n-sigma separation
0
1
2
3
4
5
Rich Technical Review, 5th September 2013, JLab
Confirmed by prototype
measurements
Notes: 9 vs 8

## Slide 20
E12-09-07:
Studies of partonic distributions using
semi-inclusive production of Kaons
E12-09-08: Studies of Boer-Mulders Asymmetry in Kaon Electroproduction with Hydrogen and Deuterium Targets
E12-09-09:
Studies of Spin-Orbit Correlations in Kaon Electroproduction in DIS with polarized hydrogen and deuterium targets
CLAS12
CLAS12
RICH detector for flavor separation of quark spin-orbit
correlations in nucleon structure and quark fragmentation
Kaon Program @ CLAS12
20
Contalbrigo M.
Rich Technical Review, 5th September 2013, JLab
Notes: Prendeire talks di Hafidi e/o Francesca ?

## Slide 21
RICH detector for
flavor separation in
covering so far
unexplored quark
valence region
C12-11-111:
Transverse spin effects in
SIDIS at 11 GeV with a
Transversely polarized target
using the CLAS12 Detector
Kaon Program @ CLAS12
21
Contalbrigo M.
Rich Technical Review, 5th September 2013, JLab
Notes: Bacup quelle per pretzelosity e wrom gear

## Slide 22
Conclusions
22
Contalbrigo M.
Interference with CLAS12:
 Designed to fit into the LTCC clearance
 No impact on the downstream detector performances
 Background occupancy at a manageable level
RICH Operation:
 Use physics triggers for commissioning and calibration
 Use well-known maximum-likelihood methods to
reconstruct the not-trivial Cherenkov signal pattern
 Use CLAS12 standard solutions for gas system and slow-control
The RICH detector allows hadron ID in the full CLAS12 kinematics
ensuring the approved physics program to be accomplished
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8