## Slide 1
RICH Project Overwiev
Contalbrigo Marco
INFN Ferrara
Rich Project Review, 5th September 2013

## Slide 2
DC
R3
R2
R1
EC
Torus
FTOF
PCAL
HTCC
Solenoid
RICH
The CLAS12 Spectrometer
2
Rich Technical Review, 5th September 2013, JLab
Contalbrigo M.
RICH: Hadron ID
for flavor separation
(common to SIDIS approved exp.)
Luminosity up to 1035 cm-2 s-1
Broad kinematic range coverage
(current to target fragmentation)
H and D polarized targets
Highly polarized electron beam
PAC30 report (2006): Measuring the kaon asymmetries is likely to be
as important as pions …. The present capabilities of the present
CLAS12 design are weak in this respect and should be strengthened.
Beam

## Slide 3
E12-09-07:
Studies of partonic distributions using
semi-inclusive production of Kaons
E12-09-08: Studies of Boer-Mulders Asymmetry in Kaon Electroproduction with Hydrogen and Deuterium Targets
E12-09-09:
Studies of Spin-Orbit Correlations in Kaon Electroproduction in DIS with polarized hydrogen and deuterium targets
CLAS12
CLAS12
RICH detector for flavor separation of quark spin-orbit
correlations in nucleon structure and quark fragmentation
Kaon SIDIS Program @ CLAS12
3
Contalbrigo M.
Rich Technical Review, 5th September 2013, JLab
Notes: Prendeire talks di Hafidi e/o Francesca ?

## Slide 4
4
Contalbrigo M.
SIDIS Kinematics @ CLAS12
Out-bending particles
In-bending particles
Rich Technical Review, 5th September 2013, JLab
A rejection factor of 1:500 is needed to suppress the background from
a one-order of magnitude larger pion-proton flux to a few % level
Notes: 9 vs 8

## Slide 5
5
Contalbrigo M.
SIDIS Kinematics @ CLAS12
Rich Technical Review, 5th September 2013, JLab
Pion mis-ID
Kaon mis-ID
kaon
pion
A pion rejection factor of 1:500 for a 90% kaon efficiency corresponds to
a 4s separation in the time (TOF) or angular (Cherenkov) distributions
n-sigma separation
5
4
0
1
2
3
1
10-1
10-2
10-3
10-4
p mis-ID
90% kaon efficiency
Notes: 9 vs 8

## Slide 6
6
Contalbrigo M.
Baseline PID @ CLAS12
HTCC (electron ID):
High Threshold Cherenkov Counter
FTOF (< 3 GeV/c hadron ID):
Forward Time-of-Flight system
LTCC (pion ID):
Low Threshold Cherenkov Counter
HTCC
LTCC
FTOF
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 7
7
Contalbrigo M.
FTOF @ CLAS12
Two scintillators panels for hadron ID:
5 cm thick, 32-375 cm long slabs
Panel 1a: from CLAS, 15 cm wide
Panel 1b: new, 6 cm wide
Combined expected resolution: 45-80 ps
4s = 0.18 ns
Suitable hadron separation achieved
by time-of-flight at 650 cm from IP:
Up to 2.8 GeV/c (q = 36 degrees)
Up to 3.6 GeV/c (q = 5 degrees)
Rich Technical Review, 5th September 2013, JLab
4s = 0.32 ns
Notes: 9 vs 8

## Slide 8
8
Contalbrigo M.
HTCC @ CLAS12
New detector for electrons ID:
CO2 radiator
48 5” quartz window PMTs
Hermetic with uniform response
Expected p.e. number with electrons ~ 16
Pions in-efficiency for minimum 2 p.e. number:
100% below 5 GeV/c (Cherenkov threshold)
~ % level around 6 GeV/c
~ few per mil above 7 GeV/c
Rich Technical Review, 5th September 2013, JLab
4s cut
1 Npe
2 Npe
3 Npe
p
Pion in-efficiency
for minimum Npe
Npe
Electrons
Pions
Requested pion separation achieved above 7 GeV/c
No kaon-proton separation
Notes: 9 vs 8

## Slide 9
9
Contalbrigo M.
LTCC @ CLAS12
Derived from CLAS for pion ID:
C4F10 radiator
Complicated design with irregular response
Limited f acceptance
Expected p.e. number with electrons ~ 9
Pions in-efficiency for minimum 2 p.e. number:
100 % below 2.7 GeV/c (Cherenkov threshold)
~ % level around 5 GeV/c
~ per mil level above 7 GeV/c
Rich Technical Review, 5th September 2013, JLab
Npe
Electrons
Pions
4s cut
1 Npe
2 Npe
3 Npe
Pion in-efficiency
for minimum Npe
Requested pion separation achieved above 8 GeV/c
No kaon-proton separation
Notes: 9 vs 8

## Slide 10
Aerogel mandatory to separate hadrons in the 3-8 GeV/c momentum range with the required large rejection factors
  collection of visible Cherenkov light
  use of PMTs
Challenging project, need to minimize detector area covered with expensive photodetectors
CLAS12 Momentum Range
10
Contalbrigo M.
SIDIS
kinematics
TOF
Rich Technical Review, 5th September 2013, JLab
Ratio K/ ~ 0.1-0.15

## Slide 11
11
Contalbrigo M.
SIDIS Kinematics @ CLAS12
Intermediate angular range (15-25o)
important to reach high PT values
High Momentum region important as
transient to hard semi-exclusive region
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 12
PT distribution
12
Contalbrigo M.
RICH Requirements
z distribution
Full momentum coverage from 3 up to 8 GeV/c
Pion rejection above 3 GeV/c
Proton rejection above 5 GeV/c
Angular coverage reaching
above 20 and up to 25 degrees
Contamination limited at the few % level
Pion rejection close to 500
Proton rejection close to 100
1
10-1
10-2
10-3
10-4
p mis-ID
90% kaon efficiency
n-sigma separation
0
1
2
3
4
5
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 13
RICH
RICH
RICH
13
Contalbrigo M.
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
Glasgow University (Glasgow, UK)
J. Gutenberg Universitat Mainz (Mainz, Germany)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
The CLAS12 RICH
RICH goal: p/K/p identification from 3 up to 8 GeV/c and 25 degrees
~4s pion-kaon separation for a pion rejection factor ~ 1:500
Rich Technical Review, 5th September 2013, JLab

## Slide 14
14
Contalbrigo M.
RICH Base Configuration
1st sector by the end of FY16: one year before
unpolarized and longitudinal polarized target
physics runs
2nd++ sector important for transverse target
physics runs (left-right symmetry and statistics)
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 15
CLAS12 Geometry Constraints
15
Contalbrigo M.
25o
FTOF wall
DC3
TORUS
538 cm
124 cm
Base Numbers
 5 m from IP
 ~ 1 m gap
 Several m2 surface
Charged
particle
Proximity gap
Radiator
Photon detector
Proximity RICH
Rich Technical Review, 5th September 2013, JLab

## Slide 16
Radiator

## Slide 17
Aerogel Radiator
17
Contalbrigo M.
Rich Technical Review, 5th September 2013, JLab

## Slide 18
Aerogel Transmission Length
18
Contalbrigo M.
pinhole drying process
crack free
“initial alcogel”
  “Pinhole drying (PD)” method:
  artificially shrinks alcogel to obtain high index
  Transparency doubled for n>1.05 aerogel
M. Tabata @ RICH 2010
A.F. Danilyuk @ RICH 2010
Rich Technical Review, 5th September 2013, JLab
Aerogel Tests
(L. Pappalardo)

## Slide 19
BELLE II test-bench
15 p.e. with aerogel of
n ~ 1.05 refractive index
and 4 cm thickness
HERMES experiment
10 p.e. with aerogel of
n ~ 1.03 refraction index
and 5 cm thickness but
lower transmittance
LHC-B
7 p.e. with aerogel of
n ~ 1.03 refraction index
and 5 cm thickness but
64% packing factor
5 8 5 8 5 8 5 8 5 8 5 8
P (GeV/c)
Mean p.e. Number (5-8 GeV/c)
19
Contalbrigo M.
Rich Technical Review, 5th September 2013, JLab
New geo
Notes: Qual e’ il packing factor di HERMES ?
Refraction or refractive ?

## Slide 20
BELLE II test-bench
15 p.e. with aerogel of
n ~ 1.05 refractive index
and 4 cm thickness
HERMES experiment
10 p.e. with aerogel of
n ~ 1.03 refraction index
and 5 cm thickness but
lower transmittance
LHC-B
7 p.e. with aerogel of
n ~ 1.03 refraction index
and 5 cm thickness but
64% packing factor
5 8 5 8 5 8 5 8 5 8 5 8
P (GeV/c)
Mean p.e. Number (5-8 GeV/c)
20
Contalbrigo M.
CLAS12 Prototype
n=1.05, 2 cm
Rich Technical Review, 5th September 2013, JLab
New geo
Notes: Qual e’ il packing factor di HERMES ?
Refraction or refractive ?

## Slide 21
HERMES experiment
7.6 mrad single photon
resolution, dominated
by the ~ 2 cm pixel size
LHC-B
3 mrad single photon
resolution with ~ 3 mm comparable pixel size
5 8 5 8 5 8 5 8 5 8 5 8
P (GeV/c)
21
Contalbrigo M.
Mean p/K Separation (5-8 GeV/c)
Rich Technical Review, 5th September 2013, JLab
New geo
Notes: Fino a che energia lavora bene l’aerogel di HERMES ?

## Slide 22
HERMES experiment
7.6 mrad single photon
resolution, dominated
by the ~ 2 cm pixel size
LHC-B
3 mrad single photon
resolution with ~ 3 mm comparable pixel size
5 8 5 8 5 8 5 8 5 8 5 8
P (GeV/c)
22
Contalbrigo M.
CLAS12 Prototype
n=1.05, 2 cm
6 mm pixel size
Mean p/K Separation (5-8 GeV/c)
Rich Technical Review, 5th September 2013, JLab
RICH Prototype
(M. Mirazita)
New geo
Notes: Fino a che energia lavora bene l’aerogel di HERMES ?

## Slide 23
PhotoDetector

## Slide 24
24
Contalbrigo M.
Photon Detectors: MA-PMT
Rich Technical Review, 5th September 2013, JLab
✓ Mature and reliable technology
✓ Large Area (5x5 cm2)
✓ High packing density (89 %)
✓ 64 6x6 mm2 pixels cost effective device
✓ High sensitivity on visible towards UV light
✓ Fast response
The only option to keep the schedule is the use
of multi-anode photomultipliers (we consider the
promising SiPM technology as the alternative)
H8500 Tests
(M. Hoek)
Notes: 9 vs 8

## Slide 25
25
Contalbrigo M.
Magnetic Field
B (Gauss)
x (cm)
Y (cm)
The torus fringe-field allows the use of
Multi-Anode Photomultipliers
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 26
26
Contalbrigo M.
109 n/cm-2/year
at 1035 cm-2s-1
Radiation Damage: Neutrons
Gammas:
Neutrons:
Neutrons:
Rich Technical Review, 5th September 2013, JLab
Measured fluence @ Belle:
90/fb  1-10 109 n/cm2
Expected fluence @ Belle-2:
50/ab  2-20 1011 n/cm2
Expected fluence @ LHCB-2:
1 year  6 1011 n/cm2
Notes: 9 vs 8

## Slide 27
27
Contalbrigo M.
MA-PMTs Readout
Rich Technical Review, 5th September 2013, JLab
Front-End Electronics
(E. Cisbani)
DAQ and Trigger
(C. Cuevas)
VME DAQ Optics FPGA module
Developed for GLUEX and JLAB12
MAROC3 Front-End card with digital and
analog readout tested with the prototype
DREAM Front-End card developed
for JLAB12 micromegas readout
Basic components with
already existing designs
and prototypes
Notes: 9 vs 8

## Slide 28
The Mirror System

## Slide 29
29
Contalbrigo M.
Goals:
instrument only forward region
reduce active area (~1 m2/sector)
minimize interference with TOF system
Low material budget
Direct & reflected photons
The Mirror System
Mirrors to focus the Cherenkov
light of particles emitted at
angles J > 13 deg.
HTCC
Rich Technical Review, 5th September 2013, JLab
Notes: ----- Meeting Notes (11/11/11 14:49) -----
DIce che mettere cavi fra PMTs e eletrtonica per
singolo fotone puo' essere un problema
----- Meeting Notes (11/11/11 15:38) -----
Fregarsene della geometria e fare ray tracking!!!

## Slide 30
30
Contalbrigo M.
Direct rings for high momentum particle
 best performance !
The Mirror System
Minimize photon detector area  cost !
Open detector close to beam line  background !
Reflected rings for low momentum particle
 less demanding
Minimum interference with TOF
Multiple passages within aerogel  photon losses
Focalising mirrors allow for thicker aerogel
(to partly compensate the loss of photons)
plane
mirror
spherical
mirror
photon detector
aerogel
1 cm
3 cm
gap
Aerogel
Spherical mirrors
Photo-detectors
Planar
mirrors
Proximity Focusing RICH + Mirrors
Rich Technical Review, 5th September 2013, JLab
2
6
Integration in CLAS12
(M. Contalbrigo)

## Slide 31
31
Contalbrigo M.
Mirror Technology
Thin glass skin on a flat support
for planar mirrors
Metalized Carbon Fiber substrate
for spherical mirror
Cost-effective technology for precise
large area mirrors
(applications in terrestrial telescopes)
Self-supporting structure with
minimal material budget
(applications in physics experiments)
MAGIC-II telescope
LHCB mirror
Rich Technical Review, 5th September 2013, JLab
Mechanical Design
(S. Tomassini)
standard technologies already in use and commercially available
Notes: 9 vs 8

## Slide 32
32
Contalbrigo M.
RICH Project Achievements
2010:
✔ Concept of Design and Technology
2011:
✔ Tests of components and small prototype
2012:
✔ July: Test-beam with Electrons (Frascati)
✔ July: Test-beam with Hadrons (CERN)
✔ December: Test-beam with Hadrons (CERN)
2013:
✔ February: Start Engineering Phase
✔ 26-27 June: Technical Review
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 33
33
Contalbrigo M.
Technical Review Outcome
Rich Technical Review, 5th September 2013, JLab
Very fruitful discussion and positive response:
“A talented and dedicated collaboration is aggressively pursuing the development of a detector
that would significantly enhance the capabilities of the CLAS-12 baseline design. Retrofitting a
detector into predetermined constraints is always a challenge. Much progress has already been
made. Although several challenges remain, the panel offers their strong encouragement to
continue. The potential gain is high.”
14 valuable recommendations:
We implement actions for all.
Many are addressed already in the TDR and in the presentations.
More details are provided in the backup slides of this talk.
Notes: 9 vs 8

## Slide 34
34
Contalbrigo M.
RICH outlook
Summer 2013:
✔ August: Finalize CLAS12 RICH Project (TDR)
✔ August: Finalize Project Management Plan
✔ 5-6 September: Project Review with DOE
✔ September: Ready for Construction
GOAL: 1st sector ready by the end of FY16
Rich Technical Review, 5th September 2013, JLab
Management Plan
(P. Rossi)
Notes: 9 vs 8

## Slide 35
35
Contalbrigo M.
Technical Review Recommendations
We recommend that a full Monte Carlo of CLAS with a RICH sector be developed.
A report should be generated for review by CLAS management to document the simulation
and the expected performance of CLAS with a RICH, both the enhanced performance in
Kaon separation as well as the extent of any degradation in the response of other CLAS
components.
A full RICH simulations was implemented in the CLAS12 GEMC simulation
platform under construction: the result are reported in chapter 13 of TDR
and in the “Integration in CLAS12” talk.
2) We recommend that at least average properties such as index of refraction, transmission and
clarity be measured and recorded for each tile prior to installation. We recognize the added
potential challenge to the tight time constraints and urge the collaboration to develop procedures
required to expedite such a chain of measurements.
See answer to recommendation n.3.
3) We recommend that, given the large tile size, the variation of the index of refraction across a
tile be measured for a sample of tiles, and the typical variation be included in the RICH Monte
Carlo.
Improved and extended procedures are being defined as described in chapter 3 of TDR and
in the “Aerogel Tests” talk: a semi-automatized characterization of each tile is foreseen.
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 36
36
Contalbrigo M.
Technical Review Recommendations
4) We recommend that the collaboration obtain samples of Novosibirsk tiles fabricated with
smooth planar surfaces and assess their optical properties.
A new dedicated production will start beginning of September 2013.
5) We recommend that the collaboration investigate the potential background from scintillations
in the gas within the RICH chamber and the affect on the Aerogel of any mitigating measures.
We estimate a manageable maximum 4 p.e. background for a 1m pure-N2 gap.
An even smaller yield is expected with dry air or CO2
6) We recommend that a Finite-Element-Analysis (FEA) be undertaken for the entire detector,
considering all loads generated in transport, installation, and maintenance.
The analysis was done for the RICH structure, the mirrors and aerogel supports
for different orientations of the RICH sector as reported in chapter 10 of TDR
and in the “Mechanical Design” talk. Dedicated transport and installation
procedures will be finalized in parallel with the mechanical design.
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 37
37
Contalbrigo M.
Technical Review Recommendations
7) We recommend that the collaboration focus R&D efforts to develop a reliable time line that
leads to a mirror system which can be adequately characterized prior to installation.
We adopt standard technologies commercially available. The construction plan
is discussed in the “Project Management” document and talk.
8) We recommend that aging studies be initiated to check the long-term effects on the dark
current of the H8500 when operated at 1075 V.
To run at 1075 V is not anymore required thanks to an improvement of the
MAROC3 front-end card. Aging tests are anyway planned in September 2013.
9) We recommend that a procedure be developed to provide some characterization of the pixel
by pixel response of each MAPMT, possibly through a gain measurement in response to uniform
illumination.
An automatized pico-second laser test bench is already in operation as shown
in chapter 7 of TDR and in the “H8500 Tests” talk. An online pixel by pixel gain
calibration is foreseen by analog readout of SPE dark counts, see chapter 8 of
TDR and Front-End electronics talk.
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 38
38
Contalbrigo M.
Technical Review Recommendations
We recommend that the collaboration analyze and adopt a firm decision date, at which
point they revert to H8500 MAPMTs, at least for this first RICH sector, if Hamamatsu cannot
demonstrate mass production of H12700 units.
The chosen deadline (1st February 2014) accounts for the H12700 estimated
production time as discussed in the “Project Management” talk.
We recommend that the collaboration develop a full plan for the readout and DAQ with
a cost analysis to identify responsibilities for design, construction and implementation.
The task sharing between INFN (Front-End) and JLab (DAQ) optimizes the
complementary competences. Cost analysis and construction plan are
discussed in the “Project Management” document and talk.
12) We recommend that Jlab/Hall-B provide a defined volume for the RICH detector, including
available cooling and cabling spaces, as well as defining the required attachments to the forward
carriage.
The RICH is design to fit into the LTCC clearance and weight with same joints to
the forward carriage, as discussed in chapter 10 of TDR and “Mechanical Design”
talk. The service (HV and LV cabling, readout optical fibers and gas lines) route
and connectors along the torus coil shadow mimic the ones of LTCC.
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8

## Slide 39
39
Contalbrigo M.
Technical Review Recommendations
We recommend that Jlab/Hall-B provide a suitable limiting temperature in the region of the
FTOF and that the collaboration demonstrate by calculation that this limit can be held. Suitable
steps should be taken to protect against a failure of the airflow.
The power consumption of the readout electronics (~400 W) is discussed in
chapter 8 of TDR and in the “Front-End” talk. Standard temperature mitigating
measures and slow-control monitors exist to keep the temperature below the
100 F (38 C) limit, as shown in chapter 10 of TDR and “Mechanical Design” talk.
We recommend that the collaboration develop a detailed work-breakdown that includes the
resources required for each step in order to track closely the schedule.
The Project Plan is ready and discussed in the “Management Plan” document
and talk.
Rich Technical Review, 5th September 2013, JLab
Notes: 9 vs 8