## Slide 1: RICH studies for CLAS12
L. Pappalardo
1
Contalbrigo Marco
Luciano Pappalardo
INFN Ferrara

## Slide 2
General framework: GEMC (Maurizio, JLab) + RICH impl. (Ahmed, Argonne)
Moving to gemc
GEANT4 toolkit for a complete simulation:
realistic geometry / detailed optic effects
full Cherenkov ring simulation chain
track multiplicity / background
L. Pappalardo
2
Notes: 2

## Slide 3
Goals:
instrument only forward region
reduce active area (~1 m2/sect)
minimize interference with TOF system
Low material budget
Direct & reflected photons
The focusing mirror system
L. Pappalardo
3
Notes: 3

## Slide 4
elliptical mirror within gap volume for backward reflections
plane mirror just beyond radiator for forward reflections
combined reflections focalize Cerenkov photons onto photon-detector plane
The focusing mirror system
L. Pappalardo
4
Notes: 4

## Slide 5
Progresses done (1)
Optimization of mirror geometry to minimize the “dead region” (reflected photons were not focalized on detector at certain intermediate angles)
Optimization of RICH geometry -> joint sectors
L. Pappalardo
5
In all studies ~1m2 photon detector per sector

## Slide 6
Progresses done (2)
Investigate multi-layer (2 or more) aerogel options: e.g. thicker radiator at larger angles (more photons produced in case of reflection) to compensate for absorption in multiple crossing of radiator material
plane
mirror
spherical
mirror
photon detector
aerogel
1 cm
3 cm
gap
 Thickness 2-4-6-8-10 cm
L. Pappalardo
6

## Slide 7
Progresses done (3)
Investigate different configurations (semi-reflective mirror in front of aerogel)
Reconstruction algorithm (so far only used for systematic studies on number of p.e.)
Semi-reflective plane mirror
spherical
mirror
photon detector
aerogel
1 cm
3 cm
gap
 …but no real improvements in number of p.e.
L. Pappalardo
7

## Slide 8
(the hypothesis that maximizes is assumed to be true)
is the probability of a hit given the kinematics of track t and hypothesis h
is the hit pattern from data
= 1 if the ith PMT is hit
= 0 if the ith PMT is not hit
is the probability of no hit
is the total number of expected PMT hits
is a background term
The reconstruction algorithm

## Slide 9
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm
L. Pappalardo
9
Mirror: 14-25o
PMTs: UBA
The reconstruction algorithm

## Slide 10
Hit prob
Hit prob > 3 10-3
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm
L. Pappalardo
10
Mirror: 14-25o
PMTs: UBA
The reconstruction algorithm
Event
photon hits
Hadron expected
patterns (200 trials)
Direct
Reflected

## Slide 11
Low angles more challenging
The same with increased
number of trials
LHp-LHk,p : Mirror 14-25o PMTs: UBA
L. Pappalardo
11
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm

## Slide 12
N p.e. > 5 for reflected rings
N p.e. > 12 for direct rings
Average N p.e. : Mirror 14-25o PMTs: UBA
L. Pappalardo
12
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm

## Slide 13
n=1.06 better for patter
recognition in the presence
of backgrouns
n=1.06
L. Pappalardo
13
Average N p.e. : Mirror 14-25o PMTs: UBA
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm

## Slide 14
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm
Average N p.e. : Mirror 14-25o PMTs: UBA
Mirror is mandatory for positive
hadrons and gives benefit for
negative hadrons at large angles
and small energy
L. Pappalardo
14

## Slide 15
L. Pappalardo
15
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm
At least SBA PMTs are needed
Average N p.e. : Mirror 14-25o

## Slide 16
Average N p.e. : PMTs: SBA
Mirror up to 35o:
Worse for positive hadrons
Better for negative hadrons
L. Pappalardo
16
200 trials per point
Aerogel:
- n=1.06
- thick. increasing
with radius:
2-4-6-8-10 cm

## Slide 17
Mirror 14-35
PMT: SBA
200 trials per point
Aerogel:
- n=1.06
- thick. increasing with radius:
2-4-6-8-10 cm
2-2-10-10-10 cm
3-5-5-10-10 cm
2-4-6-6-6 cm
With 2-10 middle-angles improve
With 3-10 only small angles improve
Average N p.e. : Aerogel thickness (SBA)
L. Pappalardo
17
Notes: Mettere specchi sulla :w
pipe!

## Slide 18
Mirror 14-35
PMT: SBA
200 trials per point
Aerogel:
- n=1.06
- thick. increasing with radius:
2-4-6-8-10 cm
2-2-10-10-10 cm
3-5-5-10-10 cm
2-4-6-6-6 cm
With 2-10 middle-angles improve
With 3-10 only small angles improve
Average N p.e. : Aerogel thickness (SBA)
L. Pappalardo
18
Notes: Mettere specchi sulla :w
pipe!

## Slide 19
Mirror 14-35
PMT: SBA
200 trials per point
Aerogel:
- n=1.06
- thick. increasing with radius:
2-4-6-8-10 cm
2-2-10-10-10 cm
3-5-5-10-10 cm
2-4-6-6-6 cm
With 2-10 middle-angles improve
With 3-10 only small angles improve
Average N p.e. : Aerogel thickness (SBA)
L. Pappalardo
19
Notes: Mettere specchi sulla :w
pipe!

## Slide 20
Aerogel:
- n=1.06
- thick. increasing with radius:
6-6-6-10-10 cm
- varied semiaxes:
370 vs 370 cm (standard)
340 vs 340 cm
340 vs 370 cm
No big sensitivity on curvature
Average N p.e. : Mirror Geometry (SBA)
L. Pappalardo
20
Mirror 14-35
PMT: SBA
200 trials per point
Notes: Vedere se mirror parte da PIPE

## Slide 21
Aerogel:
- n=1.06
- thick. increasing with radius:
6-6-6-10-10 cm
Same Np.e. with increased
aerogel thickness (reduced
Cereknov angle resolution)
Can improve high angles only
Average N p.e. : Semi-reflective Mirror (SBA)
L. Pappalardo
21
Mirror 14-35
PMT: SBA
200 trials per point
Notes: Vedere se mirror parte da PIPE

## Slide 22
Aerogel:
- n=1.06
- thick. increasing with radius:
6-6-6-10-10 cm
Same Np.e. with increased
aerogel thickness (reduced
Cereknov angle resolution)
Can improve high angles only
Average N p.e. : Semi-reflective Mirror (SBA)
L. Pappalardo
22
Mirror 14-35
PMT: SBA
200 trials per point
Notes: Vedere se mirror parte da PIPE

## Slide 23
Aerogel:
- n=1.06
- thick. increasing with radius:
6-6-6-10-10 cm
Same Np.e. with increased
aerogel thickness (reduced
Cereknov angle resolution)
Can improve high angles only
Average N p.e. : Semi-reflective Mirror (SBA)
L. Pappalardo
23
Mirror 14-35
PMT: SBA
200 trials per point
Notes: Vedere se mirror parte da PIPE

## Slide 24
Aerogel:
- n=1.06
- thick. increasing with radius:
6-6-6-10-10 cm
Improve a little for negatives
at low angles
Average N p.e. : Mirrors around Pipe (SBA)
L. Pappalardo
24
Mirror 14-35
PMT: SBA
200 trials per point
Notes: Vedere se mirror parte da PIPE

## Slide 25
At low momentum the likelihood fails in events with few p.e.
(mimicing a proton close to Cerenkov threshold)
RICH performances: Mirror 14-35 SBA MA-PMTs
L. Pappalardo
25
Negative 3-3.5 GeV/c @ 23o

## Slide 26
L. Pappalardo
26
Positive 3.5-4 GeV/c @ 20o
At large angles, positive particles got smaller number of p.e.
(larger cross talk with protons)
RICH performances: Mirror 14-35 SBA MA-PMTs

## Slide 27
L. Pappalardo
27
Positive 6-7 GeV/c @ 11o
At large momentum a small pion-kaon contamination emerges
(pion and kaon rings start to touch each other)
RICH performances: Mirror 14-35 SBA MA-PMTs

## Slide 28
L. Pappalardo
28
Positive 7-10 GeV/c @ 5o
The pion mis-identification stays below 1 % at highest momenta
RICH performances: Mirror 14-35 SBA MA-PMTs

## Slide 29
Aerogel provides a good pion/kaon separation up to 8 GeV/c
Systematic studies performed with a GEANT3-based simulation provided an optimal configuration for the RICH in terms of pions/kaons separation
RICH simulation is now being performed with GEMC (GEANT4-based)
- realistic geometry & optic effects
- mirror system (different geometries tested)
- joint sectors
- multi-aerogel thickness
- semi-reflective plane mirror
A new reconstruction algorithm allows for quantitative studies (ongoing):
n of p.e. for different configurations
/K/p separation
Given the complex geometry, large surface to cover and torus bending, some
compromise has to be found. It would depend on a realistic background estimate.
Conclusions
L. Pappalardo
29

## Slide 30: Back up

## Slide 31
L. Pappalardo
31
JLAB12 Coll. Meeting Nov. 2010
Optimal
geometry
5 8 5 8 5 8 5 8 5 8 5 8
P (GeV/c)
Mean p/K separation (5-8 GeV/c)
- small photo-detector pads ( 0.3 cm)
- small radiator thickness ( 3 cm)
- relatively small refraction index ( 1.03)
Notes: Fino a che energia lavora bene l’aerogel di HERMES ?
31

## Slide 32
L. Pappalardo
32
JLAB12 Coll. Meeting Nov. 2010
Optimal
geometry
5 8 5 8 5 8 5 8 5 8 5 8
P (GeV/c)
Mean p/K separation (5-8 GeV/c)
- small photo-detector pads ( 0.3 cm)
- small radiator thickness ( 3 cm)
- relatively small refraction index ( 1.03)
Notes: Fino a che energia lavora bene l’aerogel di HERMES ?
32

## Slide 33
Average N p.e. : PMTs: UBA
Mirror 14-25o
Mirror 14-35o
Worse for positive hadrons
Better for negative hadrons
L. Pappalardo
33

## Slide 34
LHp-LHk,p : PMTs: UBA
Mirror 14-25o
Mirror 14-35o
Worse for positive hadrons
Better for negative hadrons
L. Pappalardo
34

## Slide 35
100 trials per point
Aerogel:
- n=1.06
- thick. increasing with radius:
2-4-6-8-10 cm
M35 is acceptanble but slightly
worse for positive and does
not improve at large angles ?!
Average N p.e. : Mirror Angle Coverage (UBA)
L. Pappalardo
35
Notes: Vedere se le dimensioni sono a partire da PIPE
Vedere come mai ho Npe a piu’ di 25 gradi nel caso pos m25

## Slide 36
100 trials per point
Aerogel:
- n=1.06
- thick. increasing with radius:
2-4-6-8-10 cm
Symmetric Ellipsoide
Semi-Axes focalizing onto the
photon detector best in Npe
Average N p.e. : Mirror Semi-axes (UBA)
L. Pappalardo
36