## Slide 1
Test of Innovative Photon detectors
And Integrated Electronics
For the Large-Area CLAS12 RICH
Contalbrigo Marco
INFN Ferrara
On behalf of the CLAS12 RICH Group
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Mettere tutti I nomi ?

## Slide 2
CHL-2
Upgrade magnets and power supplies
Enhance equipment in existing halls
add Hall D
(and beam line)
2
Contalbrigo M.
Beam Energy 12 GeV
Beam current 90 mA
Beam polarization 85 %
CEBAF Upgrade at Jefferson Lab
7th NDIP Conference, 2nd July 2014, Tours - France
Nucleon structure & Nuclear effects
Hybrid mesons (gluonic excitations)
Low-energy tests of SM
Heavy photon search

## Slide 3
The CLAS12 Spectrometer
3
Contalbrigo M.
Luminosity up to 1035 cm-2 s-1
Broad kinematic range coverage
(current to target fragmentation)
H and D polarized targets
Highly polarized 12 GeV electron beam
Ongoing upgrade of the CLAS detector.
First beam expected in 2016.
RICH
RICH
Beam
Hadron ID wanted for flavor separation
3D structure of the nucleon by
polarized deep-inelastic scattering
Crucial for the study of parton dynamics related to angular momentum and spin-orbit effects with flavor sensitivity.
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 4
The CLAS12 Spectrometer
4
Contalbrigo M.
Luminosity up to 1035 cm-2 s-1
Broad kinematic range coverage
(current to target fragmentation)
H and D polarized targets
Highly polarized 12 GeV electron beam
Ongoing upgrade of the CLAS detector.
First beam expected in 2016.
2 sectors to accomplish physics program,
1st sector by the end of 2016
Hadron ID wanted for flavor separation
3D structure of the nucleon by
polarized deep-inelastic scattering
Crucial for the study of parton dynamics related to angular momentum and spin-orbit effects with flavor sensitivity.
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 5
5
Contalbrigo M.
The CLAS12 RICH Requirements
cover 3-8 GeV/c momentum range up to 25 degrees
1:10 kaon w.r.t. pion flux  p rejection 1:500 required
Aerogel to separate hadrons with the required rejection factors
  collection of visible Cherenkov light
Use of PMTs: challenging project, need to minimize the detector
area covered with expensive photo-detectors
7th NDIP Conference, 2nd July 2014, Tours - France
Aerogel

## Slide 6
1 m
Lateral Flat Mirrors
Spherical Mirror
PMTs Electronic Panel
Aerogel Wall
RICH Module General Assembly
6
Contalbrigo M.
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 7
7
Contalbrigo M.
Photon Detectors: MA-PMT
✓ 64 6x6 mm2 pixels cost effective device
✓ High sensitivity on VIS towards UV light
✓ Mature and reliable technology
✓ Large Area (5x5 cm2)
✓ High packing density (89 %)
✓ Fast response
The only option to keep the schedule is the use
of multi-anode photomultipliers (we consider the
promising SiPM technology as the alternative)
Torus fringe fields in the
RICH photo-detector area
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Direzione campo magnetico ? E fringe fields

## Slide 8
MAROC3 Front-End Electronics
8
Contalbrigo M.
64 binary outputs with time jitter ~300 ps
Laser Light
Noise
(Rate saturated)
Self-trigger (dark counts)
gain equalization &
threshold selection
SPE
(ATLAS)
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Developed form Medial Imaging
Dire che 300 ps per singolo photon
Dire che analog and digital sono indipendenti e vanno sincronizzati
Chiedere a Matteo se e’ la soglia o il gain ad essere unico per chip e non per canale

## Slide 9
MAROC3 Front-End Electronics
9
Contalbrigo M.
64 binary outputs with time jitter ~300 ps
Laser Light
Noise
(Rate saturated)
Self-trigger (dark counts)
gain equalization &
threshold selection
SPE
Multiplexed analog output
(ATLAS)
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Developed form Medial Imaging
Dire che 300 ps per singolo photon
Dire che analog and digital sono indipendenti e vanno sincronizzati
Chiedere a Matteo se e’ la soglia o il gain ad essere unico per chip e non per canale

## Slide 10
RICH
beam
RICH
GEM
GEM
scintillators
(trigger)
threshold gas Cerenkov
(p/K separation)
beam
pions
few % kaons
RICH Prototype at CERN-T9
K,p
p
10
Contalbrigo M.
Gas
Cherenkov
signal
GEM
chamber
layout
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 11
Proximity Focusing RHIC Prototype
11
Contalbrigo M.
p=8 GeV/c
K (x40)
p
P (x40)
Clear hadron separation up to the CLAS12 maximum momentum
Ring Coverage ~ 80%
p=6 GeV/c
P (GeV/c) | sc (mrad) | sq (mrad) | ns
6 | 306.5 | 1.41 | 6.9
7 | 306.8 | 1.40 | 4.7
8 | 307.6 | 1.40 | 3.9
qC (mrad)
qC (mrad)
Radiator
H8500
beam
1m gap
8 GeV
beam
Aerogel: n=1.05
2cm thickness
7th NDIP Conference, 2nd July 2014, Tours - France
H8500 meets CLAS12 RICH requirements:

## Slide 12
12
Contalbrigo M.
7th NDIP Conference, 2nd July 2014, Tours - France
H8500
Q1
H12700
with optimized dynode structure:
✓ higher collection efficiency
✓ better SPE resolution
✓ enhanced cathode sensitivity
✓ slighter lower gain
✓ modest increase of dark current
H8500
H12700
H12700
s1
MA-PMT ps Pulsed Laser Test
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 13
The Novel H12700 MA-PMT
13
Contalbrigo M.
Jlab Acceptance Test Stand
Typical higher dark current for border pixels
7th NDIP Conference, 2nd July 2014, Tours - France
Gain
Gain
H8500 @ 1 kV
H12700 @ 1 kV
SPE Resolution
SPE Resolution
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 14
14
Contalbrigo M.
The SiPM Test Prototype
Custom SiPM matrices with
a pre-amplification stage
Commercial SiPM matrix
1.5 m coaxial cables
to the electronics:
SuperB derived discrimination
board + commercial TDCs
Water-cooled Peltier cell
for temperature control
[-25 : +25 Celsius]
Beam
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Rivedere Peltier cell

## Slide 15
15
Contalbrigo M.
The Custom SiPM Matrix@ -25o
Signal occupancy (%)
Background occupancy (%)
Peak RMS
Largely insensitivity to
Vbias and discriminator
threshold
High threshold
Medium threshold
Low threshold
Vbias
Vbias
For a 12 cm radius Cherenkov cone and
a 3 mm SiPM pixel, an occupancy of 4 %
corresponds to about 24 p.e.
7th NDIP Conference, 2nd July 2014, Tours - France
Vbias
Notes: Nella risoluzione entra anche il trigger!!!

## Slide 16
16
Contalbrigo M.
The Custom SiPM Matrix@ -25o
Signal occupancy (%)
Background occupancy (%)
Peak RMS
Largely insensitivity to
Vbias and discriminator
threshold
In a +/- 3 ns window
Comparable with H8500
High threshold
Medium threshold
Low threshold
Vbias
Vbias
Vbias
For a 12 cm radius Cherenkov cone and
a 3 mm SiPM pixel, an occupancy of 4 %
corresponds to about 24 p.e.
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Nella risoluzione entra anche il trigger!!!

## Slide 17
SiPM Prototype Results
17
Contalbrigo M.
Time resolution derived from time difference of SiPM
hits after removal of the single channel vs trigger offsets:
- minor residual contributions from geometry
- dominated by discriminator threshold jitter
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Developed form Medial Imaging
Dire che 300 ps per singolo photon
Dire che analog and digital sono indipendenti e vanno sincronizzati
Chiedere a Matteo se e’ la soglia o il gain ad essere unico per chip e non per canale

## Slide 18
SiPM Prototype Results
18
Contalbrigo M.
Spatial resolution improves with
SiPM hit-time analysis: iteratively
reject the farthest hit in time if
time difference > 0.8 ns (3 sigmas)
Time resolution derived from time difference of SiPM
hits after removal of the single channel vs trigger offsets:
- minor residual contributions from geometry
- dominated by discriminator threshold jitter
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Developed form Medial Imaging
Dire che 300 ps per singolo photon
Dire che analog and digital sono indipendenti e vanno sincronizzati
Chiedere a Matteo se e’ la soglia o il gain ad essere unico per chip e non per canale

## Slide 19
109 n/cm-2/year
at 1035 cm-2s-1
Neutron Irradiation Tests
19
Contalbrigo M.
7th NDIP Conference, 2nd July 2014, Tours - France
Enea
JLab
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 20
MA-PMT Irradiation Tests
20
Contalbrigo M.
-- Before
-- After ~3 years
No long-term effect on MA-PMT or MAROC3, null or negligible
effects expected on specific components after ~ 20 years of CLAS12
7th NDIP Conference, 2nd July 2014, Tours - France
PMT window:
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 21
SiPM Irradiation Tests
21
Contalbrigo M.
7th NDIP Conference, 2nd July 2014, Tours - France
S12572-015-P
3x3 mm2 Hamamatsu MPPC, 15mm cell
ASD-RGB3S-P-50
3x3 mm2 AdvanSiD SiPM, 50mm cell
New @ 22o
After 3x109 neq @ 0o
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 22
22
Contalbrigo M.
RICH Front-End Electronics
ADAPTER BOARD
ASIC BOARD
FPGA BOARD
FPGA board
ASICs board
Compatible with MA-PMTs or SiPM Matrices
7th NDIP Conference, 2nd July 2014, Tours - France
PHOTON
DETECTOR

## Slide 23
23
Contalbrigo M.
RICH Project Landscape
GOAL: 1st sector ready by the end of 2016
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
Glasgow University (Glasgow, UK)
J. Gutenberg Universitat Mainz (Mainz, Germany)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
RICH goal: 4s p/K/p separation from 3 up to 8 GeV/c
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 24
After-Pulses
24
Contalbrigo M.
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 25
SiPM Annealing
25
Contalbrigo M.
3x3 mm2 Hamamatsu MPPC, 15mm cell
3x3 mm2 AdvanSiD SiPM, 50mm cell
New @ 22o
After 3x109 neq @ 0o
After 3x109 neq @ 0o
New @ 22o
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 26
SiPM Annealing
26
Contalbrigo M.
3x3 mm2 Hamamatsu MPPC, 15mm cell
3x3 mm2 AdvanSiD SiPM, 50mm cell
New @ 22o
After 3x109 neq @ 0o
during annealing
After 3x109 neq @ 0o
during annealing
New @ 22o
Annealing at 50o
Annealing at 50o
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 27
27
Contalbrigo M.
The Hybrid Optics Design
Direct rings and best performance for high momentum particles
4.2 m
3.7 m
1.2 m
p
Beam
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 28
28
Contalbrigo M.
The Hybrid Optics Design
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
Minimize active area (cost) to about 1 m2
Material budget concentrated where TOF is less effective
Focalizing mirrors allow thick radiator for good light yield
Time resolution < 1 ns to distinguish direct and reflected patterns
Direct rings and best performance for high momentum particles
Reflected rings for less demanding low momentum particles
4.2 m
3.7 m
1.2 m
p
Beam
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 29
29
Contalbrigo M.
The Hybrid Optics Design
Aerogel
Spherical mirrors
Photo-detectors
Planar
mirrors
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
Minimize active area (cost) to about 1 m2
Material budget concentrated where TOF is less effective
Focalizing mirrors allow thick radiator for good light yield
Time resolution < 1 ns to distinguish direct and reflected patterns
Direct rings and best performance for high momentum particles
Reflected rings for less demanding low momentum particles
7th NDIP Conference, 2nd July 2014, Tours - France

## Slide 30
MA-PMT SPE Resolution
30
Contalbrigo M.
Gain
SPE Resolution
Efficiency
SPE Resolution
SPE Resolution
Gain
Gain
H8500 @ 1 kV
H12700 @ 1 kV
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 31
Aerogel Radiator
31
Contalbrigo M.
Achieved ~ 0.00050 mm4 cm-1 clarity
for 115x11.5 cm2 tiles at n=1.05*
(comparable with LHCb at n=1.03)
*Budker and Boreskov Institutes of Novosibirsk
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: Numero di LHCb e’ diverso (prendere talk di Clara)
Capire storia di AMS, perche’ loro vogliono uniformita’ spinta ?
L’n sposta il ring in modo sistematico… . Non lo miglioro con il numero di p.e.

## Slide 32
32
Contalbrigo M.
The Custom SiPM Matrix @ +25o
Signal occupancy (%)
Background occupancy (%)
Peak RMS
Equalization of the
single SiPM is critical
In a +/-3 ns window
challenging 10-3 level
High threshold
Medium threshold
Low threshold
Vbias
Vbias
Vbias
7th NDIP Conference, 2nd July 2014, Tours - France
Notes: 9 vs 8

## Slide 33
Novel H12700 MA-PMT
33
Contalbrigo M.
Jlab Acceptance Test Stand
Typical higher dark current for border pixels
7th NDIP Conference, 2nd July 2014, Tours - France
1:2 typical gain variation
Pixel Number
Hamamatsu, JLab
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 34
34
Contalbrigo M.
H8500 MA-PMT Characterization
Up to 1:4 pixel gain variation can be
compensated by the read-out electronics
H8500
Gain
SPE Loss
7th NDIP Conference, 2nd July 2014, Tours - France
H8500 Pixel SPE Loss
SPE loss limited to ~15% above 1040V
and almost uniform over 28 MA-PMTs
Notes: Ma e’ vero 1:2 su tutti e i 28 PMTs ? Altrimenti dico cosa non vera.
Quanti sono i canali “morti” e/o quanti casi oltre i 1:2
Vedere che selezione abbiamo per MA-PMTs…. Forse dark count, non uniformita’