## Slide 1
The Large-Area Hybrid-Optics
CLAS12 RICH Detector:
Test of Innovative Components
Contalbrigo Marco
INFN Ferrara
On behalf of the CLAS12 RICH Group
RICH 2013 Workshop, 2nd December 2013, SVC - Japan
Notes: Mettere tutti I nomi ?

## Slide 2
CHL-2
Upgrade magnets and power supplies
Enhance equipment in existing halls
add Hall D
(and beam line)
2
Contalbrigo M.
Beam Energy 12 GeV
Beam current 90 mA
Beam polarization 85 %
CEBAF Upgrade at Jefferson Lab
RICH 2013, 2nd December 2013, SVC - Japan
Nucleon structure & Nuclear effects
Hybrid mesons (gluonic excitations)
Low-energy tests of SM
Heavy photon search

## Slide 3
The CLAS12 Spectrometer
3
Contalbrigo M.
Hadron ID wanted for flavor separation
Luminosity up to 1035 cm-2 s-1
Broad kinematic range coverage
(current to target fragmentation)
H and D polarized targets
Highly polarized 12 GeV electron beam
Ongoing upgrade of the CLAS detector.
First beam expected in 2016.
RICH 2013, 2nd December 2013, SVC - Japan
3D structure of the nucleon by
polarized deep-inelastic scattering
Crucial for the study of parton dynamics related to angular momentum and spin-orbit effects with flavor sensitivity.
Beam

## Slide 4
The CLAS12 Spectrometer
4
Contalbrigo M.
Luminosity up to 1035 cm-2 s-1
Broad kinematic range coverage
(current to target fragmentation)
H and D polarized targets
Highly polarized 12 GeV electron beam
Ongoing upgrade of the CLAS detector.
First beam expected in 2016.
RICH 2013, 2nd December 2013, SVC - Japan
RICH
RICH
Beam
Hadron ID wanted for flavor separation
3D structure of the nucleon by
polarized deep-inelastic scattering
Crucial for the study of parton dynamics related to angular momentum and spin-orbit effects with flavor sensitivity.

## Slide 5
The CLAS12 Spectrometer
5
Contalbrigo M.
Luminosity up to 1035 cm-2 s-1
Broad kinematic range coverage
(current to target fragmentation)
H and D polarized targets
Highly polarized 12 GeV electron beam
Ongoing upgrade of the CLAS detector.
First beam expected in 2016.
RICH 2013, 2nd December 2013, SVC - Japan
2 sectors to accomplish physics program,
1st sector by the end of 2016
Hadron ID wanted for flavor separation
3D structure of the nucleon by
polarized deep-inelastic scattering
Crucial for the study of parton dynamics related to angular momentum and spin-orbit effects with flavor sensitivity.

## Slide 6
6
Contalbrigo M.
The CLAS12 RICH Requirements
RICH 2013, 2nd December 2013, SVC - Japan
cover 3-8 GeV/c momentum range up to 25 degrees
1:10 kaon w.r.t. pion flux  p rejection 1:500 required

## Slide 7
7
Contalbrigo M.
The CLAS12 RICH Requirements
RICH 2013, 2nd December 2013, SVC - Japan
cover 3-8 GeV/c momentum range up to 25 degrees
1:10 kaon w.r.t. pion flux  p rejection 1:500 required
Aerogel to separate hadrons with the required rejection factors
  collection of visible Cherenkov light
Use of PMTs: challenging project, need to minimize the detector
area covered with expensive photo-detectors

## Slide 8
8
Contalbrigo M.
The Hybrid Optics Design
Direct rings and best performance for high momentum particles
RICH 2013, 2nd December 2013, SVC - Japan
4.2 m
3.7 m
1.2 m
p
Beam
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g

## Slide 9
9
Contalbrigo M.
The Hybrid Optics Design
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
Minimize active area (cost) to about 1 m2
Material budget concentrated where TOF is less effective
Focalizing mirrors allow thick radiator for good light yield
Time resolution < 1 ns to distinguish direct and reflected patterns
Direct rings and best performance for high momentum particles
Reflected rings for less demanding low momentum particles
RICH 2013, 2nd December 2013, SVC - Japan
4.2 m
3.7 m
1.2 m
p
Beam

## Slide 10
10
Contalbrigo M.
The Hybrid Optics Design
Aerogel
Spherical mirrors
Photo-detectors
Planar
mirrors
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
plane
mirror
spherical
mirror
photon detector
aerogel
2 cm
6 cm
gap
p
g
Minimize active area (cost) to about 1 m2
Material budget concentrated where TOF is less effective
Focalizing mirrors allow thick radiator for good light yield
Time resolution < 1 ns to distinguish direct and reflected patterns
Direct rings and best performance for high momentum particles
Reflected rings for less demanding low momentum particles
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 11
Aerogel Radiator
11
Contalbrigo M.
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 12
Aerogel Characterization
12
Contalbrigo M.
Achieved ~ 0.00050 mm4 cm-1 clarity
for 115x11.5 cm2 tiles at n=1.05*
(comparable with LHCb at n=1.03)
*Budker and Boreskov Institutes of Novosibirsk
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Numero di LHCb e’ diverso (prendere talk di Clara)
Capire storia di AMS, perche’ loro vogliono uniformita’ spinta ?
L’n sposta il ring in modo sistematico… . Non lo miglioro con il numero di p.e.

## Slide 13
Aerogel Characterization
13
Contalbrigo M.
Achieved ~ 0.00050 mm4 cm-1 clarity
for 115x11.5 cm2 tiles at n=1.05*
(comparable with LHCb at n=1.03)
*Budker and Boreskov Institutes of Novosibirsk
RICH 2013, 2nd December 2013, SVC - Japan
Refractive index map
Notes: Numero di LHCb e’ diverso (prendere talk di Clara)
Capire storia di AMS, perche’ loro vogliono uniformita’ spinta ?
L’n sposta il ring in modo sistematico… . Non lo miglioro con il numero di p.e.

## Slide 14
Aerogel Chromatic Dispersion
14
Contalbrigo M.
Measured by prisma method:
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Qual e’ il packing factor di HERMES ?
Refraction or refractive ?

## Slide 15
Aerogel Chromatic Dispersion
15
Contalbrigo M.
Measured by prisma method:
fit
MC
Expected value from density:
n2(400nm) = 1+0.438r
n(400nm) = 1.0492
Measured by prototype with optical filters:
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Qual e’ il packing factor di HERMES ?
Refraction or refractive ?

## Slide 16
16
Contalbrigo M.
Photon Detectors: MA-PMT
✓ Mature and reliable technology
✓ Large Area (5x5 cm2)
✓ High packing density (89 %)
✓ 64 6x6 mm2 pixels cost effective device
✓ High sensitivity on visible towards UV light
✓ Fast response
The only option to keep the schedule is the use
of multi-anode photomultipliers (we consider the
promising SiPM technology as the alternative)
28 H8500:
14 with standard
window (H8500C)
14 with UV window
(H8500C-03)
2 H12700:
za003 and za0014
Torus fringe fields in the
RICH photo-detector area
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Direzione campo magnetico ? E fringe fields

## Slide 17
17
Contalbrigo M.
MA-PMT Gain Map
Up to 1:4 pixel gain variation can be
compensated by the read-out electronics
H8500
Gain
SPE Loss
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Ma e’ vero 1:2 su tutti e i 28 PMTs ? Altrimenti dico cosa non vera.
Quanti sono i canali “morti” e/o quanti casi oltre i 1:2
Vedere che selezione abbiamo per MA-PMTs…. Forse dark count, non uniformita’

## Slide 18
18
Contalbrigo M.
MA-PMT Gain Map
Up to 1:4 pixel gain variation can be
compensated by the read-out electronics
H8500
H12700 1:2 gain variation
Gain
SPE Loss
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Ma e’ vero 1:2 su tutti e i 28 PMTs ? Altrimenti dico cosa non vera.
Quanti sono i canali “morti” e/o quanti casi oltre i 1:2
Vedere che selezione abbiamo per MA-PMTs…. Forse dark count, non uniformita’

## Slide 19
H8500 Pixel SPE Loss
19
Contalbrigo M.
MA-PMT SPE Loss
SPE loss limited to ~15% above 1040V
and almost uniform over 28 MA-PMTs
Gain
SPE Loss
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Con VME no amplification, n shaper, 3sigma cut
MAROC amplification gain 4 e cut a 5sigma
Add plots con singolo channel ….
Fare scatter plot

## Slide 20
H8500 Pixel SPE Loss
20
Contalbrigo M.
MA-PMT SPE Loss
SPE loss limited to ~15% above 1040V
and almost uniform over 28 MA-PMTs
Gain
SPE Loss
H12700 features a significant better SPE
resolution than H8500 at similar gain
RICH 2013, 2nd December 2013, SVC - Japan
HV = 1040 V
MA-PMT Gain
MA-PMT Gain
Gain x 106
HV = 1000 V
Notes: Con VME no amplification, n shaper, 3sigma cut
MAROC amplification gain 4 e cut a 5sigma
Add plots con singolo channel ….
Fare scatter plot

## Slide 21
MAROC3 Front-End Electronics
21
Contalbrigo M.
64 binary outputs with time jitter ~300 ps
Laser Light
RICH 2013, 2nd December 2013, SVC - Japan
Noise
(Rate saturated)
Self-trigger (dark counts)
gain equalization &
threshold selection
SPE
(ATLAS)
Notes: Developed form Medial Imaging
Dire che 300 ps per singolo photon
Dire che analog and digital sono indipendenti e vanno sincronizzati
Chiedere a Matteo se e’ la soglia o il gain ad essere unico per chip e non per canale

## Slide 22
MAROC3 Front-End Electronics
22
Contalbrigo M.
64 binary outputs with time jitter ~300 ps
Laser Light
RICH 2013, 2nd December 2013, SVC - Japan
Noise
(Rate saturated)
Self-trigger (dark counts)
gain equalization &
threshold selection
SPE
Multiplexed analog output
(ATLAS)
Notes: Developed form Medial Imaging
Dire che 300 ps per singolo photon
Dire che analog and digital sono indipendenti e vanno sincronizzati
Chiedere a Matteo se e’ la soglia o il gain ad essere unico per chip e non per canale

## Slide 23
Neutron Irradiation Tests
23
Contalbrigo M.
2 109 cm-2 y-1
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 24
Neutron Irradiation Tests
24
Contalbrigo M.
-- Before
-- After ~3 years
No long-term effect on MA-PMT or MAROC3, null or negligible
effects expected on specific components after ~ 20 years of CLAS12
2 109 cm-2 y-1
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Perce’ sta a 50 Hz il dark count base ? Non dovrebbe stare a 10-15 Hz ?

## Slide 25
25
Contalbrigo M.
The SiPM Test Prototype
Custom SiPM matrices with
a pre-amplification stage
Commercial SiPM matrix
1.5 m coaxial cables
to the electronics
Water-cooled Peltier cell
for temperature control
[-25 : +25 Celsius]
Beam
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Rivedere Peltier cell

## Slide 26
26
Contalbrigo M.
The Custom SiPM Matrix @ +25o
Signal occupancy (%)
Background occupancy (%)
Peak RMS
Equalization of the
single SiPM is critical
10-3 level is
challenging
High threshold
Medium threshold
Low threshold
Vbias
Vbias
Vbias
RICH 2013, 2nd December 2013, SVC - Japan
Notes: 9 vs 8

## Slide 27
27
Contalbrigo M.
The Custom SiPM Matrix@-25o
Signal occupancy (%)
Background occupancy (%)
Peak RMS
Largely insensitivity to
Vbias and discriminator
threshold
In a +/- 3 ns window
Comparable with H8500
High threshold
Medium threshold
Low threshold
Vbias
Vbias
Vbias
For a 12 cm radius Cherenkov cone and
a 3 mm SiPM pixel, an occupancy of 4 %
corresponds to about 24 p.e.
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Nella risoluzione entra anche il trigger!!!

## Slide 28
RICH
beam
RICH
GEM
GEM
scintillators
(trigger)
threshold gas Cerenkov
(p/K separation)
beam
pions
few % kaons
RICH Prototype at CERN-T9
K,p
p
28
Contalbrigo M.
Gas
Cherenkov
signal
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 29
RICH
beam
RICH
GEM
GEM
scintillators
(trigger)
threshold gas Cerenkov
(p/K separation)
beam
pions
few % kaons
RICH Prototype at CERN-T9
K,p
p
29
Contalbrigo M.
Gas
Cherenkov
signal
GEM
chamber
layout
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 30
RHIC Prototype: Direct Light Case
30
Contalbrigo M.
p=8 GeV/c
K (x40)
p
P (x40)
Clear hadron separation up to the CLAS12 maximum momentum
Ring Coverage ~ 80%
RICH 2013, 2nd December 2013, SVC - Japan
p=6 GeV/c
P (GeV/c) | sc (mrad) | sq (mrad) | ns
6 | 306.5 | 1.41 | 6.9
7 | 306.8 | 1.40 | 4.7
8 | 307.6 | 1.40 | 3.9
qC (mrad)
qC (mrad)
Radiator
H8500
beam
1m gap
8 GeV
beam
Aerogel: n=1.05
2cm thickness

## Slide 31
RHIC Prototype: Direct Light Case
31
Contalbrigo M.
p=8 GeV/c
K (x40)
p
P (x40)
Clear hadron separation up to the CLAS12 maximum momentum
RICH 2013, 2nd December 2013, SVC - Japan
Radiator
H8500
beam
1m gap
8 GeV
beam
Aerogel: n=1.05
2cm thickness
P (GeV/c) | s1pe (mrad)
14 H8500C | 4.0
14 H8500C-03 | 5.1
All H8500 | 4.6
p=6 GeV/c
qC (mrad)
qC (mrad)
qC (mrad)

## Slide 32
RHIC Prototype: Reflected Light Case
32
Contalbrigo M.
RICH 2013, 2nd December 2013, SVC - Japan
Radiator
H8500
curved mirror
beam
mirrors + aerogel
Aerogel: n=1.05
6cm thickness
Aerogel: n=1.05
2cm thickness
6 GeV beam
plane mirror
gap not
optimized
Ring Coverage ~ 60%

## Slide 33
RHIC Prototype: Reflected Light Case
33
Contalbrigo M.
<N>=13.1
<N>=5.3
With absorbers: sizeable fraction of light survives
without
absorbers
with
absorbers
and resolution is not significantly degraded
Arbitrary units
RICH 2013, 2nd December 2013, SVC - Japan
Radiator
H8500
curved mirror
beam
mirrors + aerogel
Aerogel: n=1.05
6cm thickness
Aerogel: n=1.05
2cm thickness
6 GeV beam
plane mirror
gap not
optimized
Ring Coverage ~ 60%
Notes: Dire qualcosa UV non UV

## Slide 34
RICH Simulations
34
Contalbrigo M.
direct light setup
reflected light setup
without absorbers
with absorbers
Based on measured optical characteristics and validated with RICH prototype data
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 35
pion kaon proton
The CLAS12 Hadron ID
35
Contalbrigo M.
One charged particle per sector in average:
Non trivial RICH light pattern due to reflections:
patter recognition and likelihood ID required
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 36
pion kaon proton
The CLAS12 Hadron ID
36
Contalbrigo M.
Even with a not yet optimized tuning of pattern recognition
and likelihood ID, the p contamination is of the order of 1%
pion >> kaon everywhere
TOF + HTCC
+ RICH
few % pion
contamination
One charged particle per sector in average:
Non trivial RICH light patter due to reflections:
patter recognition and likelihood ID required
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 37
pion kaon proton
The CLAS12 Hadron ID
37
Contalbrigo M.
Even with a not yet optimized tuning of pattern recognition
and likelihood ID, the p contamination is of the order of 1%
pion >> kaon everywhere
TOF + HTCC
+ RICH
few % pion
contamination
~1:500 rejection
from x5 to ~1%
One charged particle per sector in average:
Non trivial RICH light patter due to reflections:
patter recognition and likelihood ID required
RICH 2013, 2nd December 2013, SVC - Japan

## Slide 38
38
Contalbrigo M.
RICH Project Landscape
2010: Concept of Design and Technology
2011: Tests of components and small prototype
2012: Extensive tests with large-scale prototype
2013: June: Technical Review
August: TDR
September: Project Review with DOE
GOAL: 1st sector ready by the end of 2016
Starting the construction phase
RICH 2013, 2nd December 2013, SVC - Japan
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
Glasgow University (Glasgow, UK)
J. Gutenberg Universitat Mainz (Mainz, Germany)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
RICH goal: 4s p/K/p separation from 3 up to 8 GeV/c

## Slide 39
39
Contalbrigo M.
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
Glasgow University (Glasgow, UK)
J. Gutenberg Universitat Mainz (Mainz, Germany)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
The CLAS12 RICH Project
RICH goal: p/K/p identification from 3 up to 8 GeV/c and 25 degrees
~4s pion-kaon separation for a pion rejection factor ~ 1:500
~ 1 ns time resolution to distinguish direct and reflected light patterns
RICH 2013, 2nd December 2013, SVC - Japan
Forward RICH: 2 sectors to accomplish physics
program, 1st sector by the end of 2016

## Slide 40
Mirror Technology
Thin glass skin on a flat support
for planar mirrors
Metalized Carbon Fiber substrate
for spherical mirror
Cost-effective technology for precise
large area mirrors
(applications in terrestrial telescopes)
Self-supporting structure with
minimal material budget
(applications in physics experiments)
MAGIC-II telescope
LHCB mirror
Standard technologies already in use and commercially available
40
Contalbrigo M.
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Vedere se LHCb ha spechi con pelli di vetro

## Slide 41
Mirror Technology
Thin glass skin on a flat support
for planar mirrors
Metalized Carbon Fiber substrate
for spherical mirror
Cost-effective technology for precise
large area mirrors
(applications in terrestrial telescopes)
Self-supporting structure with
minimal material budget
(applications in physics experiments)
MAGIC-II telescope
LHCB mirror
Standard technologies already in use and commercially available
41
Contalbrigo M.
RICH 2013, 2nd December 2013, SVC - Japan
Notes: Vedere se LHCb ha spechi con pelli di vetro

## Slide 42
Front View
Back View
CFRP Frame
CFRP mirror can be subdivided into
more sub-mirrors (e.g. 8 instead of 4)
637 mm
507 mm
1400 mm
832 mm
CFRP Spherical Mirror
42
Contalbrigo M.
RICH 2013, 2nd December 2013, SVC - Japan
Radius tolerance <= 1%
Surface accuracy: 5 µm RMS
Surface quality: 3 nm RMS
D0 < 5 mm
Reflectivity > 90%

## Slide 43
CFRP Substrate Weight = 17 kg
Aerogel Weight  35 kg
Total Weight = 58 kg
Tiles are constrained by a mesh of stretched nylon wires
Each Glass Mirror is bonded to three independent mounting jacks.
The stiffening frame acts as holder of the aerogel tiles
Six independent sandwich-glass mirrors.
Glass Mirror  6 kg
Planar Mirror & Aerogel Holder
43
Contalbrigo M.
RICH 2013, 2nd December 2013, SVC - Japan